NAME
       DIFRES  (Unsupported Program)

                                            Tadeusz Skarzynski 22.06.87

The program compares two files containing atomic coordinates in 
a Brookhaven format and produces a list of r.m.s. differences between 
coordinates of main-chain and side-chain atoms for every residue within 
a specified range. It also lists the differences between corresponding 
temperature factors. Some statistics of the differences for the whole
specified range is presented as well.
 
The program produces plots of the differences as a plot84 file.

The Brookhaven files used in calculations
have to be sorted according to residue numbers and the sequence of atoms
in all the corresponding residues has to be identical (you can use program
BRKSORT to achieve this). However, gaps in a sequence are allowed 
(i.e. the two files can contain a different number of residues). Names 
of corresponding residues and atoms must be identical. If not, they are
not taken into account and an appropriate message is printed. 

The following keywords should be used to select required parameters:

TITLE title (up to 80 characters)

      If this card is present the title will be plotted on the resulting
      graphs.
     
TEMPERATURE  

      Produces a plot of the differences between corresponding temperature
      factors.
Both main and side are always plotted:

           Differences between the average temperature factors of 
           main-chain atoms will be plotted.

           Differences between the average temperature factors of
           side-chain atoms will be plotted.            

XYZ  

      Produces a plot of mean r.m.s. differences between coordinates of
      main-chain or/and side-chain atoms of corresponding residues.
Both main and side are always plotted:
            Mean r.m.s. differences between main-chain atoms will be plotted.
            Mean r.m.s. differences between side-chain atoms will be plotted.

XSCALE 

      Scale to increase/decrease the standard X size

YSCALE 

      Scale to increase/decrease the standard Y size

YMAX   For XYZ rms plots allows a max YMAX on the axis
       so similar plots are on the same scale (actually YMAX+1 is
       used-- see $CEXAM/difres_YMAX.exam ) adding to the MAX to 
       avoid points touching the upper limit of the box around the graph
       also if you gave YMAX 6 and there is a point with y=7, the
       program will ignore YMAX, which I think is OK


BMAX  For TEMP plots allows a BMAX on the axis
      so similar plots are on the same scale


CHARACTER   x

      Height in cms of the characters used to label the Benson plot.
      (default: CHARACTER  3.5mm)

RESIDUE  begin1 end1 (begin2 end2)
                                 
      Used to select residues from the files. The chain name (if present)
      must be combined with the residue number (ie. RESIDUE P10 P334).
      If a range for the second file is not given it will be the same 
      as for the first file. Only one RESIDUE card can be used for each 
      run of the program.

SIGX x

      The minimal value of a rms difference to be marked by single '*' in the
      printout. N (up to 6) stars will be printed for differences N times biger
      than x. (default SIGX 0.5)
      

SIGB x
      
      The minimal value of a temperature factor difference to be marked
      by single '+' or '-' in the printout. Up to 5 minuses or pluses
      can be printed. (default SIGB 3.0)

PMIN x
      
      The program will list those pairs of corresponding residues
      which have main-chain or side-chain rms differences greater
      than x. (default: PMIN 0.0  - lists all matching pairs)

BMIN x
       
      The program will list pairs of corresponding residues with
      main-chain or side-chain temperature factor differences greater
      than x. (default: BMIN 0.0)


Examples:

#!/bin/csh -f
#
#
difres XYZIN1 barph6.a\
       XYZIN2 barph9.a\
       PLOT x.plt\
       << eof
TITLE wt barnase A to B chains
XYZ 
RESI A3 A110
eof
#
difres XYZIN1 barph6.a\
       XYZIN2 barph9.a\
       PLOT b.plt\
       << eof
TITLE wt barnase A to B chains
TEMP
RESI A3 A110
eof
#
exit
----------------------------

to make the postscript file
use either:

#!/bin/csh -f
#
set psext=".ps"
set infile=$argv[1]
if ($#argv != 2) then
   set inroot=$infile:r
   set outfile=$inroot$psext
else
   set outfile=$argv[2]
endif
#
#
pltdev -in $infile     \
      -out $outfile   \
      -por           \
      -log            \
      -xpos 1.0       \
      -ypos 1.0       \
      -npict 1        \
      -start 1        \
      -lnwt 0.3      
#
cat $CCP/include/pl.header $outfile > ${outfile}.header
mv ${outfile}.header $outfile
#
exit

----------------------------------

or the latest xloggraph which will read a plot84 file
and can view and make a hard copy - ps file
(After 20 -june-1992)


BUGS:
====

The thick line is a simplification just now
will put a proper subroutine in to thicken
the line later