FFFEAR (CCP4: Supported Program)

NAME

   fffear - Fast Fourier Feature Recognition for density fitting, release
   1.9, 19/10/00

SYNOPSIS

   fffear HKLIN foo.mtz [XYZIN foo.pdb] [MAPIN foo.map] [MAXIN foo.max]
   XYZOUT bar.pdb [ SOLIN foo.msk ]
   [Keyworded input]

REFERENCE

     * K. Cowtan (1998), Acta Cryst. D54, 750-756. Modified phased
       translation functions and their application to molecular fragment
       location.

DESCRIPTION

   `fffear' is a package which searches for molecular fragments in poor
   quality electron density maps. It was inspired by the Uppsala `ESSENS'
   software (Kleywegt+Jones, 1997), but achieves greater speed and
   sensativity through the use of Fast Fourier transforms, maximum
   likelihood, and a mixed bag of mathematical and computational
   approaches (Cowtan, 1998). Currently, the main application is the
   detection of helices in poor electron density maps (5.0A or better),
   and the detection of beta strands in intermediate electron density
   maps (4.0A or better). It is also possible to use electron density as
   a search model, allowing the location of NCS elements. Approximate
   matches may be refined, and translation searches may be performed
   using a single orientation. The results are scored using an agreement
   function based on the mean squared difference between model and map
   over a masked region.

   The program takes as input an mtz file containing the Fourier
   coefficients of the map to be searched, and a search model in the form
   of a pdb file, map, or maximum likelihood target. A `fragment mask' is
   generated to cover the fragment density, and orientations and
   translations are searched to find those transformations which give a
   good fit between the fragment density and map density within the
   fragment mask.

   The program has been highly optimised using reciprocal-space rotations
   and grid-doubling FFT's, and crystallographic symmetry
   (Rossman+Arnold, 1993) giving 4-50 times speed improvement over the
   results published in 1998. The speed of the calculation is almost
   independent of the size of the model, thus the program may also be
   used for molecular replacement calculations where weak phases are
   available.

   A maximum likelihood search function is under consideration for
   furture versions.

  `fffear' Recepies

   For a map with 3.5A phases try something like this:
fffear hklin ~/hkl/gmto-unique.mtz xyzin alpha-helix-10.pdb xyzout alpha10-rot.
pdb << eof

SOLC 0.35
SEARCH STEP 10
RESO 1000.0 3.5
CENTRE ORTH   7.464  16.169  16.893
LABI FP=FP SIGFP=SIGFP PHIO=PHIB FOMO=FOM
END
eof

   At 5.0A some of the fragment density is no longer localised. This can
   cause a mismatch between the fragment and protein density. One
   solution is to use the 'FILTER MAP' keyword to match the map and
   fragment densities. A better option is to use the 5.0A maximum
   likelihood search target. The search target is provided on MAXIN, a
   model is also provided for visualisation purposes only:
fffear hklin ~/hkl/gmto-unique.mtz maxin ml-helix-9-5.0A.max xyzin ml-helix-9.p
db xyzout alpha10-rot.pdb << eof

SOLC 0.35
SEARCH STEP 15
RESO 1000.0 5.0
FILTER MAP RADIUS 6.0
CENTRE ORTH   7.464  16.169  16.893
LABI FP=FP SIGFP=SIGFP PHIO=PHIB FOMO=FOM
END
eof

   When the search model is large (i.e. molecular replacement
   calculations or density fragment serearches to find NCS of
   croos-crystal operators), the search can be foild by long range
   variations in either the map or fragment density. In this case
   filtering should be applied to both the map and the search model:
fffear hklin ~/hkl/rnase-unique.mtz mapin rnase-mol.map << eof

SOLC 0.35
SEARCH STEP 15
MASK RADI 2.5
RESO 1000.0 5.0
FILTER MAP MODEL RADIUS 6.0
CENTRE ORTH   7.464  16.169  16.893
LABI FP=FP SIGFP=SIGFP PHIO=PHIB FOMO=FOM
END
eof

   In the case of molecular replacement calculation and NCS searches it
   is important that the search model and map should be scaled correctly:
    1. To perform molecular replacement with a sharpened model (like the
       supplied helix fragments), no SCALE keyword is required. Ensure
       all the B-factors in the input pdb are set to 0.00.
    2. To perform molecular replacement with a natural-B model, specify
       SCALE NATURAL.
    3. To perform an NCS search with density cut from the same map, both
       maps will be on the smae scale already, so you must specify SCALE
       1.0 0.0.
    4. To refine the result of an MR or NCS search, use the MODEL ROTATE
       keyword with the approximate orientation, and change the SEARCH
       STEP and RANGE.

   FILTER MAP is useful in all three cases to match the mean of the map
   and the fragment.

INPUT/OUTPUT FILES

   The structure factors and estimated phases must be provided in HKLIN.
   The search model must be specified by an coordinate model or map
   fragment in XYZIN or MAPIN.

  HKLIN

   Input mtz file - This should contain the conventional (CCP4)
   asymmetric unit of data (see CAD).

   The mtz file should contain all reflections to the limit of the
   measured diffraction pattern, since all the reflections are used to
   accurately scale the data. However, only those reflection with phases,
   to the resolution limit specified by the compulsory RESOLUTION
   keyword, will actually be used in the search procedure.

  XYZIN

   Input pdb file. This may contain an arbitrary crystal header, or none
   at all. The only restriction is that the atomic coordinates are given
   in Angstroms on arbitrary orthogonal axes. The B-factors of the input
   atoms should be set to an average value of (around) zero. Normally,
   all B-factors should be equal, usless some prior information about the
   B-factors of atoms in the desired fragment is available. (It is
   legitimate for example to make the B-factors of the C-beta or Oxygen
   atoms higher).

  MAPIN

   Input map file. This may be specified as an alternative to XYZIN to
   perform a search for NCS or cross-crystal operators. The map should
   contain the search density, placed in a cubic cell. Regions of the map
   outside the search mask should be set to zero. The search map will
   usually be generated using maprot in map cutting mode, e.g.

maprot wrkin rnase-mir.map mskin rnase-mol.msk cutout rnase-mol.map << eof
MODE TO
CELL UNIT 100 100 100 90 90 90
GRID UNIT 150 150 150
AVER 1
ROTA POLAR 0 0 0
TRAN 0 0 0
eof

   If the input map is calculated for the same structure factors which
   are given to fffear, the scaling can be overidden using SCALE 1.0 0.0.

   An input coordinate file may also be provided on XYZIN. This will not
   be used for the search, but will be rotated and output for
   visualisation purposes.

  MAXIN

   Input maximum likelihood search target. This is used in the same way
   as an input map, however it also contains density variance
   information. (Special software is used for the construction of ML
   targets for fffear). ML targets are resolution dependent, so the
   appropriate target should be used in conjunction with the RESOLUTION
   keyword. XYZIN may again be used for visualisation purposes.

  XYZOUT

   Output pdb file. This contains multiple copies of the input fragment,
   rotated and translated to the positions of the best matches between
   the fragment density and and map density. The fragments are sorted in
   order of quality, with the best first. The b-factor is set to the
   value of the search function, with low values representing a good fit.

   Good matches to major secondary structure features are usually obvious
   becuase several fragments link up or overlap in sensible manners. At
   better than 4.0A resolution, the direction of the chain is commonly
   correct as well.

   The output pdb file may be further analysed with `ffjoin'.

  MAPOUT

   A map of the best fragment fit at each position in the map. Values
   closest to zero represent the best fit.

  SOLIN

   Input mask - this is used as a filter for the results. Any
   rotation/translation solutions whose centre-of-mass falls in the
   solvent (zero) region of the mask will be excluded from the output. If
   no mask is given, the whole cell is allowed.

   Generally there is no point providing a solvent mask, since the
   solvent density generally does not provide a match to atomic features.
   However this may be useful when fitting a molecular replacement map
   from a very incomplete model, to exclude hits to the MR model.

KEYWORDS

   Input is keyworded. Available keywords are: SOLC, LABIN, RESOLUTION,
   MODEL, MASK, FILTER, SEARCH, SCALE, CENTRE, GRID, FORM, TRUNCATE,
   STRUCFAC.

BASIC KEYWORDS

   (SOLC and LABIN are compulsory. RESOLUTION is strongly recommended.)

SOLC <solc> [MEAN <solvval> <protval>]

   <solc>
          solvent content for scaling. Always input the correct solvent
          content here to ensure correct scaling. 0.0=all protein,
          1.0=all solvent.

   MEAN <solvval> <protval>
          used to set mean density for solvent and protein regions. This
          affects scaling and density modification.
          <solvval> = mean density in solvent region.
          <protval> = mean density in protein region.
          (defaults 0.32, 0.43 electrons per cubic angstrom)

LABIN FP=.. [SIGFP=..] PHIO=.. [FOMO=..]

   Enough columns must be provided to allow calculation of a map. Common
   combinations include (calculated_magnitude + phase),
   (observed_magnitude + phase + weight), (weighted_magnitude + phase).

   FP
          = F magnitude

   SIGFP
          = standard deviation, 0 for unmeasured

   PHIO
          = best initial phase estimate

   FOMO
          = weight attached to PHIO

RESOLUTION <rmin> <rmax>

   Resolution range of reflections to include in the translation search
   stage of the calculation. This should be set to cover the resolution
   range for which significant phase information is available. Good
   results are obtained with phases to 4.0A or better; for larger
   fragments (10 residues or more) information may be obtained at still
   lower resolutions.
   (default is the whole range of the input mtz file)

MODEL [RADIUS <mdlrad>] [RESOLUTION <mrmax>] [BFACTOR <bfac>] [ROTATE
<alpha> <beta> <gamma>]

   Set the parameters for the model atoms.

   <mdlrad>
          is the radius over which the atomic density is calculated (as
          VDWR in sfall).

   <mrmax>
          is the resolution at which the atomic shape functions are
          calculated. At higher resolutions this should make little
          difference, however at lower resolutions a significant amount
          of the atomic density leaks out of the fragment mask, and so
          better results are obtained if the atomic shape function is
          corrected. If <mrmax> is set to zero, resolution truncation is
          disabled and the true shape function is used.

   <bfac>
          Temperature factor to add to all the atoms in the input
          fragment. By default the search is conducted in a map sharpened
          to Boverall=0. If a different type of map is used through use
          of the SCALE card, the B-factors of the model atoms should be
          adjusted accordingly.

   <alpha> <beta> <gamma>
          An initial rotation to apply to the model before starting the
          search. This rotation is included in the output rotation
          angles. Useful for doing a translation search at fixed
          orientation, or for refining an MR solution.

   Defaults: <mdlrad>=2.5A, <mrmax>=<rmax>, <bfac>=0,
   <alpha>=<beta>=<gamma>=0.

MASK [RADIUS <mskrad>]

   Set the radius of the fragment mask about the model atoms. This
   determines the volume over which the agreement between the map and the
   model are compared. Defaults: <mskrad>=2.5A.

FILTER [MAP] [MODEL] [VARIANCE] [RADIUS <fltrad>]

   Apply a filter to the map and/or model before starting the search. The
   filter may match either the local mean (default) within the filter
   radius, or it may match both the local mean and variance. This is
   useful at low resolutions or when performing MR or NCS searches.

   MAP
          apply filter to map.

   MODEL
          apply filter to search model.

   VARIANCE
          match both local mean and variance.

   <fltrad>
          radius of sphere for local mean/variance calculation.

   Defaults: do not filter either map or model, do not match variance,
   <fltrad>=5.0A

SEARCH [STEP <step>] [RANGE <beta>] [PEAKS <npeaks>] [GRID <sampling>]

   Set the parameters for the search function.

   <step>
          is the orientation step angle in degrees. At 4.0A resolution or
          better, a search step of 10 degrees is sufficient for a 10
          residue fragment. The search step should be smaller at higher
          resolutions or for larger models. A quick and dirty result may
          often be obtained with a much coarser search step, as large as
          30 degrees.

   <range>
          Set the maximum range in degrees for the search. To perform a
          translation search on a single orientation, set <range> to 0.1.
          To refine the result of a previous search, use SEARCH STEP 2
          RANGE 10 and give the approximate orientation with MODEL
          ROTATE.

   <npeaks>
          is the number of peaks in the resulting search function for
          which rotated fragment atoms will be output. Defaults:
          <step>=10degrees, <npeaks>=100.

   <sampling>
          is the factor by which the search grid is oversampled. Higher
          values give finer search grids, and potentially better results
          at the cost of time. Default: <sampling>=1.333.

SCALE [NATURAL] [<scale> <bfac>]

   Override internal scaling and scale input data by:
       F^2 = <scale> exp (<bfac> s/2) F[obs]2
   Scaling is critical to correctly fitting the density with a model. The
   data scale will be accurately determined automatically if structure
   factor magnitudes are provided to better than 4.5A, otherwise it is a
   good idea to provide a SCALE card.

   NATURAL
          place the map on an absolute scale but do not adjust the
          B-factor.

CENTRE FRAC/ORTH <x> <y> <z>

   Center the output fragment positions in an assymetric unit around <x>
   <y> <z>, given in fractional or orthogonal corrdinates in accordance
   with the preceeding keyword. Useful to put your matches in the same
   region and any model you are working on.

OTHER KEYWORDS

   Don't use these unless you really know what you are doing. In which
   case you'd better have a better idea of what you are doing than I do.

GRID <nx> <ny> <nz>

   Set the grid for the calculation. Ideally the grid spacing should be
   1/5 of the resolution of the phases, thus for 4.0A phases the grid
   spacing must be 0.8A. Spacings greater than 1/4 of the resolution will
   cause an error. Grid sampling must be a multiple of 4 and obey any
   other requirements imposed by the spacegroup.

FORM <z> <a1> <b1> <a2> <b2>

   Alternate 2-gaussian formfactor coefficient for atomic number <z>.
   f=<a1>exp(<b1>s)+<a2>exp(<b2>s). Formfactors are supplied for H, N, C,
   O, S and other atom types are scaled from these. Given that the model
   B-factors will generally be wrong, a crude approximation is sufficient
   for all common cases.

TRUNCATE <rmin> <rmax>

   Resolution range of reflections to include in the data scaling stage.
   This keyword can be used to exclude part of the input data by
   resolution cutoffs. This is generally highly inadvisable.
   (default is the whole range of the input mtz file)

STRUCFAC [REAL <rscale>] [RECIP <hscale>]

   Use a (slow) direct Fourier to calculate the model and mask structure
   factors instead of the default FFT. The REAL and RECIP keywords may
   then be used to set the spacing of the real space grid used to
   calculate the fragment density and mask, and the reciprocal space
   sampling of the fragment and mask transforms.

   <rscale>
          The spacing in Angstroms of the grid on which the fragment
          model density and mask are calculated. Default 0.5 A.

   <hscale>
          The spacing in reciprocal Angstroms of the grid on which the
          fragment and mask transforms (structure factors) are
          calculated. This grid needs to be quite fine to ensure accurate
          interpolation when the fragment transform is related. The
          default value is sufficient for a model whose longest axis is
          15A, for larger models decrease this number proportionally.
          Default 0.01 A^-1.

OUTPUT

   The output PDB file (XYZOUT) contains up to 1000 copies of the input
   molecule in decreasing order of fit to the density. For the purposes
   of visualisation I find it useful to get the header and the first 250
   C-alpha atoms from this file, as follows:
   grep 'C[AR]' XYZOUT | head -250 > ca.pdb

   The translation function map (which omits the orientation information)
   is also output on MAPOUT. This has peaks where the origins of the good
   orientations are found. If the input model has an alpha carbon at the
   origin a rough backbone trace of map regions matching the fragment may
   be obtained.

AUTHOR

   Kevin D. Cowtan, Department of Chemistry, University of York
   email: cowtan@ysbl.york.ac.uk

REFERENCES

    1. K. Cowtan (1998), Acta Cryst. D54, 750-756. Modified phased
       translation functions and their application to molecular fragment
       location.
    2. Kleywegt G. J., Jones T. A. (1997) Acta Cryst., D53, 179-185.
       Template convolution to enhance or detect structural features in
       macromolecular electron-density maps.
    3. Rossman M. G., Arnold E. (1993) International Tables for
       Crystallography Volume C, Section 2.3: Patterson and molecular
       replacement techniques (Kluwer Academic Publishers).

SEE ALSO

   fffear fragment library, ffjoin, maprot, xloggraph

EXAMPLES

   fffear