fhscal (CCP4: Supported Program)

NAME

   fhscal - Scaling of isomorphous derivative data using Kraut's method.

SYNOPSIS

   fhscal hklin foo_in.mtz hklout foo_out.mtz
   [Keyworded input]

DESCRIPTION

   Derivative to native scale factors are calculated in equi-volume
   shells in reciprocal space using Kraut's formula (ref 1), generalised
   to use both centric and acentric data, and applied to the derivative
   data. This formula takes account of the degree of heavy-atom
   substitution, but does not require the presence of anomalous
   differences.

   The program also computes a scale factor to put the isomorphous
   difference Patterson on the correct scale for the vector-space
   refinement program VECREF.

   It also possible to apply the scales to all "scaleable" columns in a
   dataset (i.e. to F+/- and to the structure intensities; see the LABIN
   keyword), and this is advisable to avoid mixtures of scaled and
   unscaled data for a single derivative. For input MTZ files with
   dataset information, FHSCAL will attempt to check and warn you
   accordingly if it detects datasets which will be output with such a
   mixture. In these cases, specifying the AUTO keyword will cause the
   appropriate scale factor to be applied automatically to all such
   columns.

INPUT CONTROL DATA

   Free format using keywords. The following keywords may be used; only
   the leading 4 characters are significant and the order is immaterial:

     AUTO BIAS, CENT, END, LABIN, LIST, RESO, SHELLS, TITLE

   The LABIN keyword is always required, the others are optional and
   assume default values if omitted. Use of BIAS 1 is recommended,
   provided the standard deviations produced by the data processing
   program (e.g. SCALA) are reliable. If in doubt, omit BIAS.

   TITLE <title>
          Title (max 100 characters).

   LIST <list>
          Number of reflections to list (for debugging purposes). Default
          = 0.

   SHELLS <nshell>
          Number of shells to divide data (aim to have at least 200
          reflections per shell). If there is more than one derivative to
          be scaled, this applies to the one with the highest resolution.
          Default = 20.

   BIAS <bias>
          Bias factor to multiply standard deviations. This is used to
          correct for the bias effect when averaging squares of
          differences. Normally this should be 1, however care should be
          taken that the standard deviations are valid; for example, some
          programs set the s.d. of a zero F to 9999; the correct value is
          sqrt(I+sigma(I))-sqrt(I). This will cause the program to give
          incorrect results; either ignore the s.d.'s by setting BIAS =
          0, or better delete or correct the reflection(s). Default = 0.

   RESOLUTION <maxres> [ <minres> ]
          Maxres and minres can be given in any order and in Angstrom
          units or as 4*sin(theta)**2/lamda**2. If specified then
          reflections outside this resolution range will be excluded from
          scaling and the output MTZ file. If the card is absent then all
          possible reflections are used for scaling and the resolution
          range of the native determines the output. If only one number
          is given it will be taken as the high resolution cutoff.

   LABIN <program label>=<file label>
          MTZ assignments, see below.

   AUTO
          Switches on AUTOmatic column selection. This option can only be
          used if the input file contains dataset information.

          It is only necessary to specify FPHn for each dataset on the
          LABIN line (except in special cases, see below). Other labels
          can also be specified if desired. The program will then try to
          identify all "scaleable" columns in the dataset, automatically
          read them in and then apply the appropriate scale factor
          determined from FPHn.

          This option is intended to prevent a mixture of scaled and
          unscaled columns within a dataset, e.g. FPHn is scaled but not
          FPHn(+) and FPHn(-). There are a couple of caveats:

         1. It is assumed that each dataset contains the information for
            one derivative.
         2. There may be problems with the automatic scaling if datasets
            contain both SIGIMEAN and SIGDPHn. This is because the
            program cannot distinguish between sigmas for intensities
            (which need to be scaled by the square of the scale factor)
            and those for other quantities (which are multiplied by the
            scale factor).
            In these cases the automatic selection will make a best guess
            at which sigma is which; the ambiguity can also be resolved
            provided that IMEAN and SIGIMEAN are explicitly set by the
            user on the LABIN line (which is safer).

   CENT
          Use only centric reflections to compute the scale factors. All
          reflections will be scaled and output.

   END
          Terminate input. Equivalent to end-of-file.

INPUT and OUTPUT FILES

   Standard MTZ reflection files are used for input (HKLIN) and output
   (HKLOUT). The following column labels are used :
        H, K, L         Standard meaning.

        FP, SIGFP       Native amplitude and sigma.

   If only 1 derivative is being scaled:
        FPH, SIGFPH     Derivative amplitude and sigma.

        DPH, SIGDPH     Derivative anomalous difference and sigma
                        (optional).

        FPH(+), SIGFPH(+), FPH(-), SIGFPH(-)
                        Derivative amplitudes and sigmas for Friedel pair
                        (optional).

   If more than 1 derivative is being scaled (up to 20 per run), the
   column labels are FPH1, SIGFPH1, [ DPH1, SIGDPH1, FPH1(+), SIGFPH1(+),
   FPH1(-), SIGFPH1(-), ] FPH2, SIGFPH2, [ DPH2 ... ] etc.

   Scales are applied to FPH, SIGFPH and DPH, SIGDPH, FPH(+), SIGFPH(+),
   FPH(-), SIGFPH(-) if present. All other columns, including those for
   which no label assignments are given, are output unchanged.

CAVEAT

   WARNING : Reflections for which there is a derivative measurement but
   no native and which have a greater value of S than any reflection for
   which both are measured, will be rejected (because no valid scale can
   be applied). The rejections must be re-incorporated later when higher
   resolution native data becomes available.

   In order to avoid losing reflections in the scaling procedure, it is
   worth considering using the dataset with the highest resolution limit
   as the reference (i.e. 'native') dataset in FHSCAL.

PRINTER OUTPUT

   After echoing the input data, a table with the following columns is
   produced for each derivative:
    1. Shell number
    2. Maximum resolution for shell
    3. Number of reflections in shell
    4. RMS FP
    5. RMS FPH
    6. RMS (K.FPH - FP) for centrics
    7. RMS (K.FPH - FP) for acentrics
    8. Smoothed scale factor for shell

   Overall scale and temperature factors are determined from a Wilson
   plot and printed with their estimated standard deviations; however the
   scale factors actually applied to the derivative data are obtained by
   interpolating the shell scale factors.

   At the end, the V factor (pseudo-cell volume) for the FFT program for
   use in computing a correctly scaled isomorphous difference Patterson
   is given:

          V' = V * C / Kv

   where V is the true cell volume, C is the completeness of the data and
   the scale factor Kv is defined below. This value should be used for
   the VF000 keyword of FFT when preparing a Patterson map for the
   program VECREF.

ERRORS

   In addition to the usual MTZ file opening errors:

   ERROR(S) IN DATA: syntax errors were found in the general equivalent
   positions. Check for spurious characters, missing commas, extra commas
   etc.

   ERROR - NO REFLECTIONS: no common reflections were found. Check column
   assignments, check reflection listing.

   NO REFLECTIONS IN SHELL n. Try using smaller number of shells.
   Reflections may be missing in a resolution range.

PROGRAM FUNCTION

   Kraut's formula can be derived by equating the Patterson origins
        K^2 . sum FPH^2  =  sum FP^2  +  sum FH^2               (1)

   where FPH, FP and FH are derivative, native and heavy-atom amplitudes
   respectively, and K is the derivative scale to be determined.

   For acentric reflections :
        <FH^2>a  ~=  2.<(K.FPH - FP)^2>                         (2)

   Elimination of the unknown FH from (1) and (2) gives a quadratic
   equation for K, the solution of which is :
        K  =  (2.sum FP.FPH  -  sqrt(4.(sum FP.FPH)^2 -
              3.sum FP^2 . sum FPH^2)) / sum FPH^2              (3)

   Note that in the original reference the leading factor given as 1/2
   should be 2. This formula is valid only for acentric reflections.
   However it can easily be generalised to include centrics by noting
   that
        <FH^2>  ~=  <M.(K.FPH - FP)^2>                          (4)

   where M = 1 for centric and 2 for acentric, so using (4) instead of
   (2) :
        K  =  (sum M.FP.FPH  -  sqrt((sum M.FP.FPH)^2 -
              sum (M+1).FP^2 . sum (M-1).FPH^2)) / sum (M-1).FPH^2
                                                                (5)

   The numerator and denominator of (5) could be zero if all reflections
   in a shell were centric; this is unlikely, but just in case the
   equivalent formula can be used instead :
        K  =  sum (M+1).FP^2 / (sum M.FP.FPH  +
              sqrt((sum M.FP.FPH)^2 - sum (M+1).FP^2 . sum (M-1).FPH^2))
                                                                (6)

   This formula is modified slightly to take into account the bias effect
   when averaging the squares of differences, i.e. the term <M.(K.FPH -
   FP)^2> is replaced by : <M.(K.FPH - FP)^2 -
   M.((K.sigma(FPH))^2+sigma(FP)^2)> where the sigma's have been
   multiplied by the BIAS factor.

   The program reads the input control data, then makes a first pass
   through the reflections to get the resolution limits (can be
   controlled by RESO card), then a second pass to flag reflections as
   centric or acentric and accumulate the sums in shells for the scale
   factors. The scale factors are calculated and smoothed, and applied in
   a third pass. The program also computes a scale factor to apply to the
   isomorphous difference Patterson for use in the program VECREF:
        Kv  =  (sum (FPH-FP)^2)c + 2.(sum (FPH-FP)^2)a)  /
               (sum (FPH-FP)^2)c + (sum (FPH-FP)^2)a)

AUTHOR

   Ian Tickle, Birkbeck College, London

REFERENCES

    1. Kraut J, Sieker LC, High DF and Freer ST, Proc. Nat. Acad. Sci.
       USA, 48, 1417-1424 (1962).

EXAMPLE

  Simple unix example script found in $CEXAM/unix/runnable/

     fhscal.exam (Kraut scaling of derivative data.).

   (A vms version found in $CEXAM/vms/fhscal.com

  Also found combined with other programs in the example script
  ($CEXAM/unix/runnable/)

     vecref.exam (Use in vector space heavy atom refinement).