POLYPOSE (CCP4: Supported Program)
                                       
NAME

   polypose - a program for superimposing many multi-domain structures
   
SYNOPSIS

   polypose xyzin1 xyzin2 ... outdir xyzout1 xyzout2 ... foo.dat
   [Keyworded input]
   
DESCRIPTION

   This program originating from R. Diamond is a program to superimpose
   several multi-domained structures. This is done in an optimal way by
   minimising the residuals between (n*(n-1)/2) pairwise comparisons. One
   of the molecules can be fixed and the others rotated to that
   orientation. Alternatively, the structures can be oriented so their
   longest dimensions are along X. Each domain is fitted to the
   equivalent domains in the other structures.
   
   EACH DOMAIN MUST CONTAIN THE SAME NUMBER OF ATOMS.
   
   The program expects coordinates in Brookhaven format and will only
   read the `ATOM' cards. Care must be taken to ensure that each file has
   the same axis definitions (NCODE number).
   
   Transformed coordinates can be written out with optionally an average
   structure. The output files will also be in PDB format with the same
   axis system as the input files. There are coordinates for each domain
   fitted, for each structure. The coordinates used for fitting the
   structure are given as REMARKs followed by the whole structure.
   
   All the equations referred to in this documentation come from
   reference [1].
   
KEYWORDED INPUT

   The program has been parameterised and the current defaults are:
   maximum number of molecules = 10, maximum number of
   sub-domains/domains = 60, maximum number of atoms in molecule = 1200,
   maximum number of atoms in a domain = 2000. The permitted data control
   statements in the form of keywords are listed below:
   
     CHECK, COMBINE, END, FIX, INCLUDE, INDEPENDENT, INPUT, MAXCYCLE,
     OUTPUT, TERMINATE
     
  MAXCYCLE <num>
  
   This determines the maximum number of cycles to achieve the best fit
   between the structures. Note that it can be set to 1 if there are just
   two structures or the structures are of the same shape. (default=10)
   
  INDEPENDENT
  
   If present this causes the residual (equation R0 #40 and #41) to be
   calculated from N(N-1)/2 distinct and independent orientations. If the
   card is not present then R0 is not calculated.
   
  INPUT [ CA | ALL ]
  
   The program will either work with all the atoms or just the C-alpha
   atoms (default) in a residue. The number of atoms in a domain MUST be
   equal between molecules.
   
  INCLUDE <res1> TO <res2> FILE <num>
  
   These define sub-domains within the <num>-th molecule. The ordering of
   the cards relates to the sub-domain number. Each molecule must contain
   the same number of sub-domains. If absent all the residues in the
   molecule are included.


e.g. INCL 1 to 10 file 4
     INCL A1 to B10 file 1

  COMBINE <num1> <num2> ... <numN>
  
   This combines sub-domains into a domain (applies to all molecules).
   Sub-domains can be included several times which has the effect of
   weighting the atoms in that sub-domain. If there is no COMBINE card
   then each sub-domain is treated as a domain. Sub-domains not mentioned
   in the COMBINE cards are treated as domains. If the number of atoms
   exceeds the maximum permitted in a domain then an error will be given.
   Note that the atoms in a domain are paired off in order between
   molecules.
   
   e.g. if there are 6 sub-domains
   
   COMB 1 2 3
   COMB 2 4
   COMB 2 6

   gives
   
   1st domain is 1 2 3
   2nd domain is 2 4
   3rd domain is 2 6
   4th domain is 5

   and
   
   COMB 1 2 2 3

   gives
   
   1st domain 1 2 3   atoms of the second sub-domain have double weight
   2nd domain 4
   3rd domain 5
   4th domain 6

  TERMINATE <crit>
  
   This defines when the the refinement will stop before reaching
   MAXCYCLE. The criterion is either when:


    SUM [ SIN{DP/2}**2 ] < <crit>

    DP = angular shift in orientation.

   or
    the reduction in rms in the cycle   <   <crit> * rms

   Default <crit>=0.00001.
   
  OUTPUT [ MATRIX | COORDS | AVERAGE ]
  
   Defines what output will be given from the program. MATRIX will just
   output the orientation matrices. COORDS will give the transformed
   coordinates (.rot), the atoms used to fit the structure will be given
   as REMARKS in the PDB file followed by the whole structure. The
   calculations will be done per domain per molecule. AVERAGE will
   produce an average structure (.ave) based on the orientation
   calculated for each domain. Each option is progressive from MATRIX to
   AVERAGE. Thus OUTPUT AVER will effectively include the other options.
   
  CHECK
  
   If the keyword is present then the program will check residue and atom
   name. The program will terminate if inconsistencies are found between
   molecules.
   
  FIX <num>
  
   The orientation of the <num>-th molecule will be fixed and the other
   structures will be fitted to this molecule. If this card is not
   present then the longest axes of the molecules will be aligned along
   x.
   
  END
  
   Terminate input.
   
INPUT AND OUTPUT FILES

   The input PDB files are assigned to logical names XYZIN1 XYZIN2 etc.
   The input keywords must use the same numbering, e.g. domains specified
   for 'file 1' should refer to XYZIN1, FIX 2 should refer to the
   molecule in XYZIN2, and so on. However, if the numbering used is not
   consecutive, the program will renumber the files, e.g. if XYZIN1,
   XYZIN2 and XYZIN4 are specified then the latter becomes structure 3.
   
   The output files are:
   
   a)
          optionally transformed coordinates <name>d<nn>.rot, where <nn>
          is the domain number. The root <name> can be assigned through
          the logical name XYZOUT1, XYZOUT2 etc. If the logical names are
          undefined then the root name of the input file is taken. If the
          logical OUTDIR is defined all coordinate files will be sent to
          this directory.
          
   b)
          optionally average coordinates <name>d<nn>.ave, where <name> is
          taken from the fixed coordinates or the first file (defined in
          a similar way to the transformed coordinates) and <nn> is the
          domain number.
          
EXAMPLES

polypose XYZIN1 dtk1.pdb XYZIN2 dtk2.pdb OUTDIR /scr1/acr/ XYZOUT1 jnk1 << +
maxcycle 3
input all
indep
include 1 to 10 file 1
include 1 to 10 file 2
include 11 to 20 file 1
include 11 to 20 file 2
combine 1 2
output average
check
fix 1
+


   The output files would be:
/scr1/acr/jnk1d01.rot
/scr1/acr/dtk2d01.rot
/scr1/acr/jnk1d01.ave

PRINTER OUTPUT

   Rms differences are shown between all structures pairwise. Also, the
   summation of these differences is shown (R1 equation #42). R1 can be
   compared with R0 (equation #40 and #41) which represents the sum of
   the rms residuals over the best possible fit between two molecules
   calculated from all possible pairs. R0 is the lowest rms achievable
   but can only be recognised in practise when all the structures are of
   the same shape or there are only two structures.
   
AUTHOR

R. Diamond
MRC Laboratory for Molecular Biology
Hills Road
Cambridge CB2 2QH
England

REFERENCES

    1. R. Diamond, Protein Science, 1, 1279-1287 (1992)