RSEARCH (CCP4: Supported Program)
                                       
NAME

   rsearch - R-factor and correlation coefficient between Fcalc and Fobs
   for positions of molecule within a specified grid.
   
SYNOPSIS

   rsearch HKLIN foo_in.mtz [ SEARCHSAVE foo_search.tmp ] [ MAPOUT
   foo_rsearch.map ]
   [Keyworded input]
   
DESCRIPTION

   When a molecule is correctly orientated in a unit cell, but the
   translation parameters are not known, RSEARCH calculates the R-factor
   and correlation coefficient between calculated and observed structure
   factors for each position of the molecule within a specified grid.
   
   You may prefer to calculate a translation function with TFFC instead
   of RSEARCH, since this is much faster.
   
   There is an option to restart RSEARCH when it runs out of time : a
   file assigned to SEARCHSAVE will record the intermediate sums for the
   R factors. These are updated after every 100th reflection and a note
   is written to the log file. There are also options (keywords CENT and
   RZONE) to limit the reflections used to centrics or a specified zone.
   
KEYWORDED INPUT

   The various data control lines are identified by keywords. Only the
   first 4 characters need be given. Those available are :
   
     AXIS, BINMAP, BGRV, CENT, CORRELATION, END, FCLIMIT, FOLIMITS,
     LABIN, LPMAP, NRFACTOR, RESOLUTION, RESTART, RZONE, SCALE,
     SYMMETRY, TITLE, XGRID, YGRID, ZGRID
     
  AXIS
  
   Order of grid axes : fast, medium, slow.
   At present, the program only looks at the slow (sectioning) axis.
   Possible inputs are therefore
                               - X Y Z
                               - Z X Y
                               - Y Z X

  BINMAP
  
   Output a map of R factors or correlation coefficients over the
   specified grid
   
  BGRV <brgval>
  
   Background R value for maps.
   Default: the average R value.
   The terms calculated are (background R value - grid R value).
   
  CENT
  
   By default, all reflections are included in the calculation. If this
   is set, ONLY centric reflections are selected. Centric zones are
   identified using the spacegroup operators.
   
  CORRELATION
  
   Turns ON the plotting of correlation maps
   
  FCLIMIT <fmaxc>
  
   Set lower limit on FC for inclusion in R factor calculation.
   
   In low symmetry space groups such as P21, you should exclude all terms
   where one calculated (partial) structure factor FC is very small,
   since then the R factor will be independent of translation.
   
  FOLIMITS <fmin> <fmax>
  
   Set upper and lower limits on observed structure factors for inclusion
   in R factor calculation (given in either order).
   
  LABIN <program label>=<file label>...
  
   Input column assignments. The program labels are:
        H  K  L  FP  SIGFP  FC1  PC1 ... FC12  PC12  FC  PHIC

   FP is the observed structure factor and SIGFP its standard error. FCn
   and PCn are the partial calculated structure factors and phases for
   symmetry operation n. Known structure may be added in by defining FC
   and PHIC.
   
  LPMAP
  
   Output a lineprinter map of R factors for all hkl and for each of 5
   resolution shells.
   
  NRFACTOR <nrfactor>
  
   Number of R factors to be listed to output file. Default is 15;
   maximum is 500.
   
  RESOLUTION [ <resmin> ] <resmax>
  
   Low and high resolution limits in either order. These are in Angstroms
   or 4(sintheta/lambda)**2 if both are <1.0. Defaults: 1000.0 2.0
   
  RESTART <nref> <ihh> <ikk> <ill>
  
   Intermediate results will have already been written to a file assigned
   to SEARCHSAVE. Calculation is restarted after the <nref>-th
   reflection; <ihh> <ikk> <ill> are the indices of the first reflection
   to be included. These 4 numbers are printed to the log file after
   every 100 reflections.
   
  RZONE <number>...
  
   5 numbers to define a reflection zone limiting reflections included in
   the R value calculation.
To define the zone -h +k +l = 3n     input RZON    -1 1 1   3 0
To define                 l = 2n +1  input RZON     0 0 1   2 1

   This keyword may be given more than once, but at present ALL
   conditions must be obeyed simultaneously.
   
  SCALE <scale> <bfact>
  
   The scale and temperature factor to be applied to observed structure
   factors FP. Defaults: 1.0 0.0.
   FP(USED) is scale*FP(INPUT)*EXP(-bfact(SINTHETA/LAMBDA)**2).
   It is sensible to run SCALEIT to put FP onto the same scale as one of
   the (partial) structure factors FCn before running RSEARCH. The scale
   here should then be approximately sqrt(nsymp), where nsymp is the
   number of primitive symmetry operators.
   
  SYMMETRY [ <nspgrp> | <namspg> ]
  
   Spacegroup number or name. You may alternatively input operators in
   X,Y,Z form. Spacegroup details are normally taken from the input MTZ
   file.
   
  TITLE <title>
  
   A title to be written to the log file.
   
  GRID SPECIFICATIONS
  
  XGRID | YGRID | ZGRID <min> <max> <n>
  
   3 parameters for each of the 3 keywords: XGRID, YGRID and ZGRID.
   
   The input is complicated to allow greater flexibility in describing
   the search volume. The first 2 parameters give the range in grid
   points, either directly or by reference to other limits given; the
   third, the number of grid points covering the unit cell in the
   appropriate direction.
   For a simple rectangular box :
    XGRID    ixmin  ixmax  nx    (3 numbers)
    YGRID    iymin  iymax  ny    (3 numbers)
    ZGRID    izmin  izmax  nz    (3 numbers)

   For a prism, there are many options.
   For example :
    XGRID    ixmin  ixmax  nx    (3 numbers)
    YGRID   xmin  iymax  ny    (1 character string, 2 numbers)
(or YGRID    iymin xmax  ny )  (number, character string, number)
(or YGRID   xmin xmax  ny )  (2 character strings, 1 number)
    ZGRID    izmin  izmax  nz    (3 numbers)

   where xmin means type the letters xmin ....

   For another sort of prism :
    XGRID    ixmin  ixmax  nx    (3 numbers)
    YGRID   xmin  iymax  ny    (1 character string, 2 numbers)
(or YGRID    iymin xmax  ny )  (number, character string, number)
(or YGRID     x    x   ny )  (2 character strings, 1 number)
    ZGRID    izmin  izmax  nz    (3 numbers)
(or ZGRID   xmin  izmax  nz )  (character string, 2 numbers)
(or ZGRID    izmin xmax  nz )  (number, character string, number)
(or ZGRID     x    x   nz )  (2 character strings, 1 number)
(or ZGRID   ymin  izmax  nz )  (1 character string, 2 numbers)
(or ZGRID    izmin ymax  nz )  (number, character string, number)
(or ZGRID     y    y   nz )  (2 character strings, 1 number)

   Note that maps can only be output if the grid is rectangular. The
   maximum total grid points in the search volume is 60000. The maximum
   number in any one direction is 1024.
   
  END
  
   End of input.
   
INPUT AND OUTPUT FILES


INPUT  : MTZ Data file assigned to HKLIN
        [File containing intermediate sums assigned to SEARCHSAVE]
OUTPUT :[File for Binary R factor map assigned to MAPOUT]

Those in parentheses are optional.

NOTES

  Memory allocation
  
   The program allocates memory dynamically. If the default isn't enough
   you can increase it by setting the logical name RSEARCH_NSIZE to the
   appropriate value indicated by the error message. (It ought to figure
   this out for itself.)
   
  Suggested procedure leading to RSEARCH
  
    1. Run LSQKAB to rotate your search coordinates by alpha beta gamma
       obtained from rotation search.
       DO NOT FORGET to change your CRYSTL and SCALE cards to those of
       the new space group.
       Remember that the rotation angles are relative to a given NCODE.
       The SCALE matrix MUST be consistent with NCODE.
       COORDCONV will generate such a matrix when it converts fractional
       coordinates to PDB format.
    2. Run SFALL to generate a list of h k l FC PC for all +-h +-k l for
       these coordinates in this cell.
    3. Run CAD to collect together H K L FP SIGFP FC1 PC1 FC2 PC2 ... for
       the unique set of intensity data.
    4. Run SCALEIT to scale FP to one of the FCn.
    5. Run RSEARCH
#
# *****************************************************************
#
#  Run sfall to calculate structure factors
#
sfall
HKLOUT sfrkall.mtz
XYZIN trans_pgk.pdb
<< END-sfall
TITLE SFS
MODE  SFCALC XYZIN
GRID  80 160 160
RESOLUTION 20 3
SYMMETRY 1
SFSGRP   1
LABOUT   FC=FC PHIC=AC
END
END-sfall
#
# *****************************************************************
#
#  Run cad to collect FP and FC's into one file.
#  Up to this stage, can use the same procedure for TFFC & RSEARCH.
#  No phase changes made to partial phases.
#
cad
HKLIN1 allderiv.mtz
HKLIN2 sfrkall.mtz
HKLOUT cad.mtz
<< END-cad
RESOLUTION OVERALL 20 3
TITLE  resolving the bacillus pgk
LABIN  FILE 1 E1=F  E2=SIGF
CTYPIN FILE 1 E1=F  E2=Q
LABIN  FILE 2 E1=FC E2=AC
CTYPIN FILE 2 E1=U  E2=V
END
END-cad
#
# *****************************************************************
#
#  Optional step
#  Run scaleit to put FP onto the same scale as one of the FC's.
#  Remember you will need to use the resolution required for RSEARCH.
#
scaleit
HKLIN cad.mtz
HKLOUT cad_sc.mtz
<< END-scaleit
TITLE Scale FP to one FCpart ready for RSEARCH
RESOLUTION 8 4
REFINE   isotropic
LABIN    FP=FC1 SIGFP=FC1 FPH1=F SIGFPH1=SIGF
CONVERGE ABS 0.0001 TOLR 0.000000001 NCYC 4
END
END-scaleit
       
EXAMPLES

   For previous stages to this, see 'NOTES'
   

#  Rfactor search
#  Input mtz hkl list of FP SIGFP FC1 PC1 FC2 PC2.....
#  R factor requires FP scaled to FC.
#  Correlation coefficient should be independent of scale.
#
rsearch
HKLIN cad_sc.mtz
MAPOUT dav.map
SEARCHSAVE dav.tmp
<< END-r
TITLE Bacillus search in a-c plane
SCALE FP 1.414 0
RESOLUTION  8 4           !  resolution limits
FOLIMITS 10 10000000000.  !  Fobs limits
FCLIMIT  50               !  Fc minimum
CORRELATION
BINMAP                    !  binary map output
AXIS  Y Z X
XGRID 0 20 40             !  grid limits
YGRID 0 1  1
ZGRID 0 40 80
LABIN FP=F SIGFP=SIGF FC1=FC1 PC1=AC1 FC2=FC2 PC2=AC2
END
END-r

AUTHOR

   Eleanor Dodson, York University