SCALA (CCP4: Supported Program)

NAME

   scala - scale together multiple observations of reflections

SYNOPSIS

   scala HKLIN foo_in.mtz HKLOUT foo_out.mtz
   [Keyworded Input]

   Keyworded input summary
   References
   Input and Output files
   Examples
   Release Notes

DESCRIPTION

   Scaling options
   Control of flow through the program
   Partially recorded reflections
   Scaling algorithm
   TAILS correction
   Data from Denzo
   Datasets
   Data harvesting

   This program scales together multiple observations of reflections, and
   merges multiple observations into an average intensity.

   Various scaling models can be used. The scale factor is a function of
   the primary beam direction, either as a smooth function of Phi (the
   rotation angle ROT), or expressed as BATCH (image) number. In
   addition, the scale may be a function of the secondary beam direction,
   acting principally as an absorption correction, either expanded as
   spherical harmonics, or as a interpolated three-dimensional function
   of Phi and the spatial coordinates of the measured spot on the
   detector. Such three-dimensional scaling is typically ill-determined,
   but it is generally useful if suitably restrained (see below for
   discussion of this). The secondary beam correction is related to the
   absorption anisotropy correction described by Blessing (Ref Blessing
   (1995) ), the interpolated three-dimensional correction is similar to
   that described by Kabsch (Ref Kabsch (1988)).

   The merging algorithm analyses the data for outliers, and gives
   detailed analyses. It generates a weighted mean of the observations of
   the same reflection, after rejecting the outliers.

   The program does three passes through the data:
    1. a scaling pass: firstly, there is an initial estimate of the
       scales, then the scale parameters are refined
    2. an analysis pass to analyse discrepancies and adjust the standard
       deviation estimates
    3. a final pass to apply scales, analyse agreement & write the output
       file, usually with merged intensities, but alternatively as a copy
       of the input file with evaluated scales appended to each
       observation.

   Normally anomalous scattering is ignored during the scale
   determination (I+ & I- observations are treated together), but the
   merged file always contains I+ & I-, even if the the ANOMALOUS OFF
   command is used. Switching ANOMALOUS ON does affect the statistics and
   the outlier rejection (qv)

Scaling options

   The optimum form of the scaling will depend a great deal on how the
   data were collected. It is not possible to lay down definitive rules,
   but some of the following hints may help.
    1. If successive images are collected with the same detector (on-line
       detector) or equivalent detectors, and the beam intensity is
       steady or smoothly varying, then use a smoothed scaling options.
       Only use the SCALE BATCH option if every image is different from
       every other one, i.e. off-line detectors (including film), or
       rapidly or discontinuously changing incident beam flux. This may
       often be the case for synchrotron data if "dose" mode is not used.
       It is possible to "mix-and'match" options. For instance, the best
       option for data from an unstable synchrotron beam may be e.g.
       SCALES BATCH BFACTOR ON BROTATION SPACING 10, which will make the
       Bfactor variation smooth, but the scales discontinuous by batch.
    2. If there is a discontinuity between one set of images and another
       (e.g. change of exposure time), then flag them as differents RUNs.
       This will be done automatically if no runs are specified.
    3. The SECONDARY correction is recommended: this provides a
       correction for absorption and is better than the DETECTOR option.
       It should always be restrained with a TIE SURFACE command (this is
       the default): under these conditions it is reasonably stable under
       most conditions, even in the absence of a reference dataset. It
       should only be combined with a B-factor if there is noticeable
       radiation damage and resolution beyond say 2.5A. The ABSORPTION
       (crystal frame) correction is similar to SECONDARY (camera frame)
       in most cases, but may be preferable if data has been collected
       from multiple alignments of the same crystal.
    4. If the SECONDARY (or ABSORPTION) correction is not used, use a
       B-factor correction, unless the data are only low-resolution.
       Traditionally, the relative B-factor is a correction for radiation
       damage (hence it is a function of time), but it also includes some
       other corrections eg absorption. For frozen crystals with little
       or no radiation damage it is better to turn off the B-factor and
       use the SECONDARY correction.
    5. The TAILS correction should be tried if the fractional bias is
       significant (this statistic is not calculated if there are no
       fully-recorded reflections). The refinement of the TAILS
       parameters is not very robust, and it may be necessary to FIX A1
       (this should be improved).
    6. When trying out more complex scaling options (eg SECONDARY,
       TAILS), it is a good idea to try a simple scaling first, to check
       that the more elaborate model gives a real improvement.
    7. For isomorphous replacement, it may be useful to provide a native
       dataset as a reference, to make the systematic errors in the
       derivative similar to those in the native (ie "local" scaling,
       using the SECONDARY option). When scaling multiple MAD data sets
       they should all be scaled together in one pass, outliers rejected
       across all datasets, then each wavelength merged seperately. This
       is now the default if multiple datasets are present in the input
       file.

   Other options are described in greater detail under the KEYWORDS.

Control of flow through the program

   Each of the stages can be individually activated or suppressed.
   Particularly useful options are:
     * Restarting scaling after a crash or failure to converge :the
       RESTORE option enables a restart from where you left off. Scales
       are dumped by default to a file SCALES after each cycle in case of
       crashes (see DUMP/NODUMP options).
     * Rerunning the merge step without repeating the scaling, using the
       ONLYMERGE and RESTORE commands, eg to adjust the SDCORRECTION
       parameters

Partially recorded reflections

   See appendix 1

   Partially recorded reflections are by default included the scaling
   pass, as well as included in the final analysis and merging. They may
   optionally be excluded from the scaling (controlled by the command
   INTENSITIES), and excluded from the final analysis (controlled by the
   command FINAL). Note that this default has changed from earlier
   versions

   The different options for the treatment of partials are set by either
   the PARTIALS command, effective for both scaling & merging stages; or
   separately for the scaling stage only (INTENSITIES command) or for the
   merging stage only (FINAL command).

   Partials may either be summed or scaled : in the latter case, each
   part is treated independently of the others.

   For datasets with few partials, with low mosaicity compared to the
   image widths, very few partials run over more than two images, &
   partial summation is not usually a problem. If you have many partials
   running over 3 or more images, you may need to tune the partial
   selection flags to accept or reject partial sets according to their
   reliability.

   Summed partials:
   All the parts are summed (after applying scales) to give the total
   intensity, provided some checks are passed. The number of reflections
   failing the checks is printed. You should make sure that you are not
   losing too many reflections in these checks.

   Scaled partials:
   In this option, each individual partial observation scaled up by the
   inverse FRACTIONCALC, provided that the fraction is greater than
   <minimum_fraction> [default = 0.5].

Scaling algorithm

   See appendix 2

TAILS correction

   The TAILS (SCALES .. TAILS) correction may be used to improve poor
   partial bias: this is an attempt to allow for the difference in scan
   width between fulls and partials. A partial is measured across twice
   (or 3 times etc) the rotation width of a full, so more of the diffuse
   scattering tails are included in the intensity, leading to an
   under-estimation of the fulls relative to partials. This correction is
   not very robust (though more so than in earlier versions of Scala),
   and the parameters may be unstable: you should always try first
   without this correction, and check that it really does improve the
   data statistics, without applying ridiculously large corrections. See
   appendix 3 for more details.

Data from Denzo

   Data integrated with Denzo may be scaled and merged with Scala as an
   alternative to Scalepack, or unmerged output from scalepack may be
   used. Both have some limitations. See appendix 4 for more details.

Datasets

   Data in MTZ files are assigned to "datasets", within a heirarchy of
   Crystal/Dataset [crystal names are not yet implemented]. A crystal
   also has a "project name" which is not part of the hierarchy but is
   used to group data for harvesting. Each of these levels of heirarchy
   has "properties": a crystal has a unit cell, and a dataset has a
   wavelength. Unmerged data files as used in Scala typically contain a
   single dataset, but may contain multiple datasets if for instance
   multiple wavelength datasets are being scaled together, or if a
   reference set is present. Each BATCH in the file is assigned to a
   specific dataset.
   Assigning a dataset:-
    1. Preferably, a project name, crystal name and dataset name should
       be assigned when the file is created, eg in Mosflm
    2. Utility programs eg REBATCH may be used to (re)assign dataset
       names and add or correct dataset properties (wavelength and cell)
    3. Names may be (re)assigned within Scala using the NAME command.
       This may be useful if names have not been assigned before, or if
       data from different crystals are merged into a single dataset.

   Using datasets in Scala:
    1. A RUN may not contain batches from different datasets, but a
       dataset may contain multiple runs. By default if runs are not
       explicitly defined, each dataset is assigned to a different run.
       Datasets may be explicitly assigned to runs (see the RUN command).
    2. By default, each dataset is written out to a different output
       file, (see OUTPUT options).
    3. By default, outliers are rejected across all datasets (unless
       REJECT SEPARATE). This is normally a sensible thing to do for MAD
       data, since the expected differences are small, but carries with
       it the danger of rejecting real differences. Suitable options
       might be:-
         ANOMALOUS ON
         REJECT 6 ALL 8  # to check between I+ and I-
       but larger numbers might be more appropriate for strong signals
       and good data
    4. Various analyses are done between datasets, comparing the
       anomalous differences and the dispersive (isomorphous) differences
       from a defined "base" set (ie correlation between ((I(i) -
       I(base)) and (I(j) - I(base)) (i .ne. j .ne. base)). Typically the
       base dataset would be a high-energy remote (this is the default),
       but it may be set with the BASE command.

Data Harvesting

   Provided a Project Name and a Dataset Name are specified (either
   explicitly or from the MTZ file) and provided the NOHARVEST keyword is
   not given, the program will automatically produce a data harvesting
   file. This file will be written to

   $HARVESTHOME/DepositFiles/<projectname>/ <datasetname>.scala

   The environment variable $HARVESTHOME defaults to the user's home
   directory, but could be changed, for example, to a group project
   directory.

   See also Data Harvesting.

KEYWORDED INPUT - SUMMARY

                      Summary classification of keywords

     * The most commonly used keywords (almost essential)

        RUN
                define subsets of data as "runs"

        SCALES
                define scaling method (scaling model)

        SDCORRECTION
                set SDcorrection parameters (particularly after first
                run). Note that the multiplie Sdfac is adjusted
                automatically, but the fraction of intensity Sdadd is
                not, but defaults to 0.02.

        REJECT
                set outlier rejection limits

        ANOMALOUS on
                anomalous scattering is present

        RESOLUTION
                resolution limits

        TITLE
                set a title

     * Control of program flow

        ONLYMERGE
                Skip the scaling, go straight to merge step: this
                requires RESTORE as well if the original input HKLIN file
                is used, but not if a file from a previous OUTPUT
                SEPARATE run is re-input.

        RESTORE
                restore previously-determined scales, eg after
                convergence failure or instead of re-running the scaling

     * General keywords:

        PARTIALS
                controls acceptance of partials

        PRINT
                how much printing in logfile

     * Principal keywords affecting scaling

        CYCLES
                number of cycles and convergence etc

        EXCLUDE
                select reliable reflections for scaling

        TIE
                restrain scaling parameters, particularly useful for the
                SECONDARY (ABSORPTION) scaling option

        LINK
                use same scaling parameters for different runs (for
                suface parameters (SECONDARY, ABSORPTION) or TAILS)

        INTENSITIES full
                use only fulls in scaling

     * Principal keywords affecting merging

        OUTPUT
                what to put in the output file

        FINAL
                treatment of partials

     * Dataset and Data Harvesting keywords

        NAME
                assign project/crystal/dataset name

        BASE
                define "base" dataset for dispersive differences

        PRIVATE
                directory permissions for user only

        USECWD
                write deposit file to current directory

        RSIZE
                width of a row in deposit file

        NOHARVEST
                do not write deposit file

     * Rarely used keywords: ANALYSE, BINS, DAMP, DUMP, FILTER, HISTORY,
       INITIAL, INSCALE, NODUMP, NOSCALE, OVERLAPMAP, SKIP, SMOOTHING,
       [UN]FIX, UNLINK, WIDTH, XYBINS

KEYWORDED INPUT - DESCRIPTION

   In the definitions below "[]" encloses optional items, "|" delineates
   alternatives. All keywords are case-insensitive, but are listed below
   in upper-case. Anything after "!" or "#" is treated as comment. The
   available keywords are:

   ANALYSE, ANOMALOUS, BASE, BINS, CYCLES, DAMP, DUMP, EXCLUDE, FILTER,
   FINAL, HISTORY, INITIAL, INSCALE, INTENSITIES, LINK, NAME, NODUMP,
   NOHARVEST, NORMALISE, NOSCALE, ONLYMERGE, OUTPUT, OVERLAPMAP,
   PARTIALS, PRINT, PRIVATE, REJECT, RESOLUTION, RESTORE, RSIZE, RUN,
   SCALES, SDCORRECTION, SKIP, SMOOTHING, TIE, TITLE, [UN]FIX, UNLINK,
   USECWD, WIDTH, XYBINS

  RUN <Nrun> [<subkeys>]

   Define a "run" : Nrun is the Run number, with an arbitrary integer
   label (i.e. not necessarily 1,2,3 etc). A "run" defines a set of
   reflections which share a set of scale factors. Typically a run will
   be a continuous rotation around a single axis. The subkeys allow
   definition of a run in a flexible way. The definition of a run may use
   several RUN commands. If no RUN command is given, or if the ALL
   keyword is used, then run assignment will be done automatically, with
   run breaks at discontinuities in dataset, batch number or Phi. Batches
   or batch ranges may still be excluded, either with the EXCLUDE subkey
   here, or by using the EXCLUDE keyword (qv)

   Subkeys:

        REFERENCE
                This run is a reference set, i.e. it will be given a
                single scale factor = 1.0 (an input scale factor in the
                SCALE column will still be applied if present)

        BATCH | <b1> <b2> <b3> ... | <b1> TO <b2> |
                Define a list of batches, or a range of batches, to be
                included in or excluded from the run. If batches are
                included in more than one run definition, the last
                definition will take priority.

        ALL
                Include all batches. In this case automatic run assigment
                will be done: to override this use eg RUN 1 BATCH 1 to
                99999

        CRYSTAL <crystal_name>
                Define a crystal name to be included in the run. This
                would usually be used in conjunction with the DATASET
                subkey. Crystal names are not defined at present, so this
                option is not very useful.

        DATASET <dataset_name>
                Define a dataset name to be included in the run. A
                crystal name may be combined with the dataset name using
                the syntax <crystal_name>/<dataset_name>. The dataset
                names used here are those present in the input file, not
                those assigned or altered by the NAME command.

        INCLUDE | EXCLUDE
                Set include/exclude flag for a following RANGE or BATCH
                keyword. Excluded batches or ranges will be omitted from
                the output file.

        RANGE <r1> TO <r2>
                Rotation range to include or exclude

   Examples:
  RUN 1 BATCH 1 TO 10000    # unconditionally include all batches
  RUN 1 ALL  EXCLUDE 77 79 132  # automatic run splitting will be done
  RUN 1 INCLUDE BATCH 1 TO 200 EXCLUDE 77 79 132
  RUN 2 CRYSTAL  Native DATASET Lambda1
  RUN 3 DATASET  Native/Lambda2
  RUN 4 INCLUDE RANGE 0 TO 90 EXCLUDE RANGE 45 TO 48

  SCALES [<subkeys>]

   Define layout of scales, ie the scaling model. Note that a layout may
   be defined for all runs (no RUN subkeyword), then overridden for
   particular runs by additional commands.

   Subkeys:

        RUN <run_number>
                Define run to which this command applies: the run must
                have been previously defined. If no run is defined, it
                applies to all runs

        ROTATION <Nscales> | SPACING <delta_rotation>
                Define layout of scale factors along rotation axis (i.e.
                primary beam), either as number of scales or (if SPACING
                keyword present) as interval on rotation [default SPACING
                10]

        BATCH
                Set "Batch" mode, no interpolation along rotation
                (primary) axis.This option is compulsory if a ROT column
                is not present in the input file, but otherwise the
                ROTATION option is preferred.

        SMOOTH <delta_batch>
                Set smoothed Batch mode: this treats the batch number as
                a rotation angle, and interpolates along rotation axis in
                the same way as the ROTATION option. <delta_batch> sets
                the interval on batches (ie the number of batches to
                smooth over). This option is an alternative to ROTATION
                if you have lost the information in the ROT column
                (spindle rotation angle (Phi)), but otherwise the
                ROTATION option is preferred.

        BFACTOR ON | OFF | ANISOTROPIC
                Switch Bfactors on or off. The default is ON, but Bfactor
                refinement will be switched off by default if the scales
                are allowed to vary across the detector or on secondary
                beam direction (qv DETECTOR, SECONDARY, ABSORPTION,
                SURFACE). The ANISOTROPIC keyword activates anisotropic
                Bfactors (NOT RECOMMENDED): beware that the parameters
                for this option is likely to be poorly determined. Note
                that the anisotropic correction is centrosymmetric.

        BROTATION [|TIME] <Ntime> | SPACING <delta_time>
                Define number of B-factors or (if SPACING keyword
                present) the interval on "time": usually no time is
                defined in the input file, and the rotation angle is
                used. SCALES BATCH BROTATION SPACING 5 make the Bfactor
                variation smooth, but the scales discontinuous by batch.

        SECONDARY [<Lmax>]
                Secondary beam correction expanded in spherical harmonics
                up to maximum order Lmax in the camera spindle frame. The
                number of parameters increases as (Lmax + 1)**2, so you
                should use the minimum order needed (eg 4 - 6). This
                correction would typically be combined with the usual
                primary beam correction (eg ROTATION SPACING 5 SECONDARY
                6). The deviation of the surface from spherical should be
                restrained eg with TIE SURFACE 0.001 [default]

        ABSORPTION [<Lmax>]
                Secondary beam correction expanded in spherical harmonics
                up to maximum order Lmax in the crystal frame based on
                POLE (qv). The number of parameters increases as (Lmax +
                1)**2, so you should use the minimum order needed (eg 4 -
                6). This correction would typically be combined with the
                usual primary beam correction (eg ROTATION SPACING 5
                ABSORPTION 6). The deviation of the surface from
                spherical should be restrained eg with TIE SURFACE 0.001
                [default]. This is not substantially different from
                SECONDARY in most cases, but may be preferred if data are
                collected from multiple settings of the same crystal, and
                you want to use the same absorption surface. This would
                only be strictly valid if the beam is larger than the
                crystal.

        SURFACE [<Lmax>]
                Local correction expanded on direction of the scattering
                vector in hkl space (ie crystal frame) in spherical
                harmonics up to maximum order Lmax. The number of
                parameters increases as (Lmax + 1)**2, so you should use
                the minimum order needed (eg 4 - 6). The polar axis may
                be specified with the POLE keyword (qv). If you want to
                do 3-dimensional scaling, the SECONDARY or ABSORPTION
                option is preferable: this option should only be used if
                the diffraction geometry information required to work out
                the beam directions is not available.

        POLE <h|k|l>
                Define The polar axis for ABSORPTION or SURFACE as h, k
                or l (eg POLE L): the pole will default to either the
                closest axis to the spindle (if known), or l (k for
                monoclinic space-groups).

        DETECTOR <Nscales_X> [<Nscales_Y>] | SPACING <delta_X>
                [<delta_Y>]
                Define layout of scale factors on detector (i.e.
                secondary beam), either as number of scales in each
                direction (along XDET & YDET), or (if SPACING keyword
                present) as interval on XDET & YDET. The values for Y
                default equal to those for X is not specified. This
                option assumes that the detector positions are recorded
                in the input file (columns XDET, YDET), in any units (mm
                or pixels). If you allow the scale to vary across the
                detector (anything other than DETECTOR 1, the default),
                then by default Bfactor refinement is switched off, since
                the combination is likely to be unstable [Default 1
                scale, i.e. no variation of scale across detector]. The
                SECONDARY option is probably better.

        CONSTANT
                One scale for each run (equivalent to ROTATION 1)

        TAILS [<v> [<a0> [<a1>]]]
                Apply correction for diffuse scattering (reflection
                tails) for this run. This can only be used with summed
                partials (INTENSITIES PARTIALS: this is the default). See
                introduction for explanation. Initial values for the
                parameters v, a0 & a1 may be given following the keyword.

             v
                    width of tails in reciprocal space (A**-1) [default =
                    0.01]
             a0
                    fraction of intensity in diffuse peak at theta = 0
                    [default = 0.0, fixed]
             a1
                    slope of intensity fraction against (sin
                    theta/lambda)**2 [default = 10]

                Parameters may be fixed using the FIX command, or the
                same set used by different runs as defined by the LINK
                command. These controls may be required to avoid the
                parameters going wild.

        SLOPE
                NOT RECOMMENDED. Set "Slope" mode, like Batch, except
                that each batch has different scales at the beginning and
                end of the rotation range. The value used for each
                reflection is interpolated linearly according to the
                "Rotation" (phi) value. SLOPE implies BATCH mode. Be
                careful with this option: does it really improve the
                data? It is unlikely to work well if the mosaicity is
                large. TIE ROTATION may be used to restrain the
                difference in scales.

  SDCORRECTION [RUN <RunNumber>] [[NO]ADJUST]
  [FULL | PARTIAL | BOTH] <Sdfac> [<SdB>] <Sdadd>

   Modifiers for input standard deviations: these are modified to
        sd(I) corrected = Sdfac * sqrt(sd(I)**2 + SdB*Ihl' + (Sdadd*Ihl)**2)

   where Ihl is the intensity (SdB may be omitted in the input and its
   use is not recommended). Default values are 1.0, 0.0, 0.02.

   RUN <run_number>
   Define run to which this command applies: the run must have been
   previously defined. If no run is defined, it applies to all runs.
   Different values may be specified for fully recorded reflections
   (FULL) and for partially recorded reflections (PARTIAL), or the same
   values may be used for both (BOTH), e.g.
         sdcorrection full 1.4 0.11 part 1.4 0.05

   The keyword NOADJUST stops the automatic adjustment of the Sdfac
   parameters from the normal probability analysis at the beginning of
   the merge stage [default is ADJUST] (this applies to all runs)

   With the output options SEPARATE or POSTREF, the modified Sds are
   written to the output file in columns SIGIC [& SIGIPRC if IPR is
   present]. These columns will be used by Postref but ignored on reinput
   to Scala.

  PARTIALS [NO]CHECK [NO]TEST [<lower_limit> <upper_limit>] CORRECT
  <minimum_fraction>] [NO]GAP MAXWIDTH <maximum_width> SCALE_PARTIAL
  <minimum_fraction> USE_PROFILE

   Select the way in which partials are treated in both scaling and
   merging. These settings may be overridden separately for the scaling
   and merging steps with the INTENSITIES and FINAL commands
   respectively.

   By default, partials are included (summed) in both scaling and in
   merging.

   Subkeys:

        [NO]CHECK
                do [not] check for consistency of MPART flags (if
                present, i.e. from Mosflm). Reflections failing this test
                are tested for total fraction (see TEST option) [default
                do if MPART is present]

        [NO]TEST [<lower_limit> <upper_limit>]
                do [not] accept partials only if total fraction (from
                FRACTIONCALC column) is in range lower_limit ->
                upper_limit [default if no MPART flag, limits 0.95, 1.05]

        CORRECT [<minimum_fraction>]
                Scale partials in range minimum_fraction -> lower_limit,
                predicted total fraction (needs reliable FRACTIONCALC)
                [default minimum = <lower_limit>]

        [NO]GAP
                do [not] accept partials with a gap in, e.g. a partial
                over 3 parts with the middle one missing. GAP implies
                NOCHECK and TEST: CORRECT may also be set [default NOGAP]

        MAXWIDTH <maximum_width>
                maximum number of parts for an acceptable summed partial

        SCALE_PARTIALS
                use scaled partials greater than <Minimum_fraction> in
                the scaling. Only use this if the FRACTIONCALC column
                contains a good estimate of the partiality.

        USE_PROFILE
                use profile-fitted intensity even for scaled partials

  INTENSITIES

          [INTEGRATED | PROFILE | PR_PART]
          [[NO]ANOMALOUS]
          [FULLS | ONLYFULLS | SCALE_PARTIAL <minimum_fraction>
          | PARTIALS [ [NO]CHECK | [NO]TEST [<lower_limit> <upper_limit>]
          [CORRECT <minimum_fraction> ] [ [NO]GAP ] [MAXWIDTH
          <maximum_width>] ] ]

   Intensities selection for scaling: which intensities to use, whether
   to keep Bijvoet pairs separate, and treatment of partials in scaling:

   (a) Intensity selection options:

   Set which intensity to use, of the integrated intensity (column I) or
   profile-fitted (column IPR), if both are present. Note this applies to
   all stages of the program, scaling & averaging.

   Subkeys:

        INTEGRATED
                summation integrated intensity I.

        PROFILE
                profile-fitted intensity IPR [default if present]. Note
                that this will not be used for scaled partials unless
                PARTIALS USE_PROFILE is set.

        PR_PART
                profile IPR for fullys, integrated for partials

   (b) Treatment of Bijvoet-related observations

   By default, all observations (I+ & I-) are treated alike in scaling.
   This is normally the correct thing to do, since the anomalous
   differences are usually small and randomly positive and negative. In a
   case with large anomalous differences and high redundancy, it may be
   better to keep the I+ & I- observations separate in the scaling. Note
   that typically this will severely reduce the scaling overlaps between
   different parts of the data, and is not recommended except in special
   cases.

   Subkeys:

        ANOMALOUS
                keep I+ and I- observations separate in scaling

        NOANOMALOUS
                use I+ and I- together in scaling [default]

   (c) Options for treatment of partials in scaling (overrides options
   given under PARTIALS):

   Set whether partially recorded reflections should be used in scaling,
   & if so, whether to use summed or scaled partials. By default summed
   partials are used in scaling as well as fulls. See introduction above
   for a description of the use of partially recorded reflections.
   Treatment of partials in the final averaging stage is defined with the
   FINAL command

   Subkeys:

        FULLS
                use fully recorded observations only, & previously summed
                partials (from MOSFLM ADDPART)

        ONLYFULLS
                use fulls only: exclude previously summed partials (from
                MOSFLM)

        SCALE_PARTIALS
                use scaled partials greater than <Minimum_fraction> in
                the scaling. Only use this if the FRACTIONCALC column
                contains a good estimate of the partiality.

        PARTIALS
                use summed partials in scaling (if present) [this is the
                default]. The following flags are qualifiers of PARTIALS
                and will override those given on a previous PARTIALS
                command, for the scaling step only (not merging):

              [NO]CHECK
                      do [not] check for consistency of MPART flags (if
                      present). Reflections failing this test are tested
                      for total fraction (see TEST option) [default do if
                      MPART is present]

              [NO]TEST [<lower_limit> <upper_limit>]
                      do [not] accept partials only if total fraction
                      (from FRACTIONCALC column) is in range lower_limit
                      -> upper_limit [default if no MPART flag, limits
                      0.95, 1.05]

              CORRECT [<minimum_fraction>]
                      Scale partials in range minimum_fraction ->
                      lower_limit, predicted total fraction (needs
                      reliable FRACTIONCALC) [default minimum =
                      <lower_limit>]

              [NO]GAP
                      do [not] accept partials with a gap in, e.g. a
                      partial over 3 parts with the middle one missing.
                      GAP implies NOCHECK and TEST: CORRECT may also be
                      set [default NOGAP]

              MAXWIDTH <maximum_width>
                      maximum number of parts for an acceptable summed
                      partial

  REJECT

   [SCALE | MERGE] [COMBINE] [SEPARATE]
   <Sdrej> [<Sdrej2>]
   [ALL <Sdrej+-> [<Sdrej2+->]]
   [KEEP | REJECT | LARGER | SMALLER]

   Define rejection criteria for outliers: different criteria may be set
   for the scaling and for the merging (FINAL) passes. If neither SCALE
   nor MERGE are specified, the same values are used for both stages. The
   default values are REJECT 6 ALL 8

   If there are multiple datasets, by default, deviation calculations
   include data from all datasets [COMBINE]. The SEPARATE flag means that
   outlier rejections are done only between observations from the same
   dataset. The usual case of multiple datasets is MAD data.

   If ANOMALOUS ON is set, then the main outlier test is done in the
   merging step only within the I+ & I- sets for that reflection, ie
   Bijvoet-related reflections are treated as independent. The ALL
   keyword here enables an additional test on all observations including
   I+ & I- observations. Observations rejected on this second check are
   flagged "@" in the ROGUES file. In the scaling step, the outlier check
   includes all observations, unless anomalous observations are kept
   separate in scaling (INTENSITIES ANOMALOUS: this is an unusual option
   for special cases only).

   Subkeys:

        SEPARATE
                rejection & deviation calculations only between
                observations from the same dataset

        COMBINE
                rejection & deviation calculations are done with all
                datasets [default]

        SCALE
                use these values for the scaling pass

        MERGE
                use these values for the merging (FINAL) pass

        sdrej
                sd multiplier for maximum deviation from weighted mean I
                [default 6.0]

        [sdrej2]
                special value for reflections measured twice [default =
                sdrej]

        ALL
                check outliers in merging step between as well as within
                I+ & I- sets (not relevant if ANOMALOUS OFF)

        sdrej+-
                sd multiplier for maximum deviation from weighted mean I
                including all I+ & I- observations (not relevant if
                ANOMALOUS OFF)[default check within I+ & I- sets only]

        [sdrej2+-]
                special value for reflections measured twice [default =
                sdrej+-]

        KEEP
                in merging, if two observations disagree, keep both of
                them [default]

        REJECT
                in merging, if two observations disagree, reject both of
                them

        LARGER
                in merging, if two observations disagree, reject the
                larger

        SMALLER
                in merging, if two observations disagree, reject the
                smaller

   The test for outliers is described in Appendix 5

  ANOMALOUS [OFF] [ON | ALL]

   [RUN <Nrun>]
   [MATCH [SPINDLE | INVERT | <hkl symmetry>]]
   [PHIDIF <maximum Phi difference>]

   Controls the treatment of anomalous scattering information in the
   merging step. Note that the option of selecting matching anomalous
   pairs is not recommended for normal use: it is likely to lead to
   seriously incomplete data in many cases, and the results should be
   compared carefully with those with the MATCH option switched off.

   Subkeys:

        OFF [default]
                no anomalous used, I+ & I- observations averaged together
                in merging

        ON | ALL
                separate anomalous observations in the final output pass,
                for statistics & merging: this is also selected the
                keyword ANOMALOUS on its own

        RUN <run number>
                set run for this MATCH option to apply to, otherwise it
                applies to all runs [default]

        MATCH
                use only matching I+ & I- pairs in merging
                Matching pairs are :-

                      (a) in same run

                      (b) related by defined symmetry (if given as
                            SPINDLE | INVERT | <hkl symmetry>)

                      (c) not more than DeltaPhi apart (if given by
                            PHIDIF)

                      Definition of symmetry:-

              SPINDLE
                      related by negation of reciprocal index closest to
                      spindle: this option requires full orientation data
                      to be present in the file

              INVERT
                      related by inversion of indices, i.e. -h, -k, -l

              <hkl symmetry>
                      specified hkl symmetry (e.g. h, -k, l)

        PHIDIF <DeltaPhi>
                maximum difference in Phi (ROT) between matching pairs

  RESOLUTION [RUN <Nrun>] [[LOW] <Resmin>] [[HIGH] <Resmax>]

   Set resolution limits in Angstrom, either order, optionally for
   individual runs (in which case this command MUST come after definition
   of the run). The keywords LOW or HIGH, followed by a number, may be
   used to set the low or high resolution limits explicitly: an unset
   limit will be set as in the input HKLIN file. If the RUN subkeyword is
   omitted, the limit applies to all runs. [Default use all data]

  TITLE <new title>

   Set new title to replace the one taken from the input file. By
   default, the title is copied from hklin to hklout

  ONLYMERGE

   Only do the merge step, no initial analysis, no scaling (== INITIAL
   NONE; NOSCALE). Note that this will usually need to be combined with a
   RESTORE command.

  RESTORE [<Scale_file_name>]

   Read initial scales from a SCALES file from a previous run of Scala
   (scales are normally dumped on every cycle, see DUMP). The number of
   scales defined for each run this time should typically be the same as
   in the dump, although a set of scale factors along ROTATION or
   DETECTOR may be extrapolated to additional batches which were not
   present in the initial scaling. The file may contain scales for runs
   which are not used this time, but new runs may not be added. RESTORing
   from a scale file which does not properly correspond to the run which
   generated the file is liable to give silly results. No initial
   analysis pass will be done unless the command INITIAL ANALYSE is
   given.

  INITIAL MEAN | UNITY | RUN <RunNumber> <InitialScale> | NONE | ANALYSE

   Define method of setting initial scales

   Subkeys:

        MEAN
                from mean intensities by rotation range [default]

        UNITY
                set all scales = 1.0

        RUN <RunNumber> <InitialScale>
                set initial scale factor for this run If this option is
                used, any runs whose scales are not set explicitly will
                have their scales set = 1.0

        NONE
                no initial analysis pass, set all scales to unity

        ANALYSE
                force initial analysis pass even if RESTORE option is
                used

  PRINT [<subkey>]

   Define amount of printing

   Subkeys:

        NONE
                almost none

        BRIEF
                some more [default]

        CYCLES
                more information about each minimization cycle

        FULL
                quite a lot

        DEBUG [<reflection_interval>]
                far too much: also define reflection interval for
                printing

        ALLOVERLAP
                print all numbers in overlap matrix after initial pass,
                rather than the default condensed table

        OVERLAP
                print condensed table of overlap matrix after initial
                pass

        NOOVERLAP
                no printing of overlap matrix after initial pass
                [default]

  CYCLES [[NUMBER] <Ncycle>] [CONVERGE <Conv_limit>] [REJECT <Rej_cycle>]
  [WEIGHT VARIANCE | UNIT ]

   Define number of refinement cycles, convergence limit, and weighting
   scheme for scale refinement

   Subkeys:

        [NUMBER]
                maximum number of cycles [default 10]

        CONVERGE
                convergence limit (multiple of sd(param)) [default 0.3]

        REJECT
                1st cycle number for rejection of outliers [default 2]
                The default is not to reject outliers on the first cycle
                when the scales may be a long way off, but if the initial
                scales are reasonable (particularly if they come from a
                previous run) it is probably better to exclude outliers
                from the first cycle as well

        WEIGHT VARIANCE | UNIT
                Weighting scheme for scale refinement: VARIANCE weighting
                is default and usual; UNIT weights may help if the
                scale-factors vary over a large range (unit weights have
                not been much tested)

  EXCLUDE [RUN <Nrun>] [[NO]EMAX <maximum_E> | EPROB <minimum_probability>]
  [SDMIN <value>] [SDMAX <value>] [ABSMAX <value>] [ARC INSIDE|OUTSIDE <X1>
  <Y1> <X2> <Y2> <X3> <Y3> ... <Xn> <Yn>] [RECTANGLE <Xmin> <Xmax> <Ymin>
  <Ymax>] [BATCH <batch range>|<batch list>] [CRYSTAL <crystal_name>] [DATASET
  <dataset_name>]

   Set intensity limits or positional limits for excluding observations.

   Limits for scaling and merging passes:-
   EMAX or EPROB, ARC, RECTANGLE, BATCH, CRYSTAL and DATASET limits apply
   to all stages of the program

   Limits for scaling pass only:-
   If an observation is considered too weak (I .lt. sd(I) * SDMIN), or if
   an observation is too strong (I .gt. sd(I) * SDMAX .or. I .gt.
   ABSMAX), then all observations of that reflection are omitted from the
   scaling. Exclusions are not applied to a Reference run. [Default
   EXCLUDE SDMIN 3.0]
   These exclusions do not apply to the initial scale calculation
   (INITIAL MEAN), nor to the output statistics, only to the scaling. The
   test is only done on fully recorded observations, and against the
   input standard deviations (i.e. unmodified by SDCORRECTION parameters)

   Subkeys:

        RUN <Nrun>
                defines a run number (previously defined) for these
                exclusion parameters to apply to: else applies to all
                runs (this applies to SD, arc and rectangle limits only:
                the EMAX|EPROB limit applies to all runs)

        EMAX <maximum_E> | EPROB <minimum_probability>
                Define maximum normalized amplitude E allowed: this may
                be given either as the maximum E-value EMAX for an
                acentric reflection eg 8 - 10, or as the minimum allowed
                probability EPROB eg 1e-8 Eprob = exp (- Emax**2).
                Excluded reflections are listed in the log file, and in
                the ROGUES file. See R.Read, CCP4 Study Weekend,
                Sheffield 1999. [Default EMAX 10]. NOEMAX switches this
                test off

        SDMIN
                minimum sd multiple for inclusion

        SDMAX
                maximum sd multiple for inclusion

        ABSMAX
                maximum absolute value i.e. observations are excluded
                if:-

                I  .lt. sd(I) * SDMIN
        .or.    I  .gt. sd(I) * SDMAX
        .or.    I  .gt. ABSMAX

        ARC
                defines an area of detector coordinates (XDET, YDET) to
                be excluded from all calculations, both scaling and
                merging, as a circular arc. Data are excluded either
                INSIDE (lower radius) or OUTSIDE (higher radius) the arc.
                The arc is defined by fitting a circle to the coordinates
                of 3 or more points: points 1 (X1,Y1) and 2 (X2,Y2)
                define the ends of the arc (in either order). If X1,Y1 =
                X2,Y2 a complete circle is excluded. A series of arcs may
                be defined. This option allows for the exclusion of
                shadows on the detector from eg backstop or cryocooler
                etc

        RECTANGLE
                defines a rectangular area of detector coordinates (XDET,
                YDET) to be excluded from all calculations, both scaling
                and merging. A series of rectangles may be defined.

        BATCH | <b1> <b2> <b3> ... | <b1> TO <b2> |
                Define a list of batches, or a range of batches, to be
                excluded altogether.

        CRYSTAL <crystal_name>
                Define a crystal name to be excluded altogether. This
                would usually be used in conjunction with the DATASET
                subkey. Crystal names are not defined at present, so this
                option is not very useful.

        DATASET <dataset_name>
                Define a dataset name to be excluded altogether. A
                crystal name may be combined with the dataset name using
                the syntax <crystal_name>/<dataset_name>. The dataset
                names used here are those present in the input file, not
                those assigned or altered by the NAME command.

  [UN]TIE [SURFACE [<Sd_srf>]] [BFACTOR [<Sd_bfac>]][A1 [<Sd_a1>]][ROTATION
  [<Sd_z>]][DETECTOR [<Sd_xy>]]

   Apply or remove restraints to parameters. These can be pairs of
   neighbouring scale factors on rotation axis (ROTATION = primary beam)
   or in detector plane (DETECTOR = secondary beam) to have the same
   value, or neighbouring Bfactors, or surface spherical harmonic
   parameters to zero (for SECONDARY or SURFACE corrections, to keep the
   correction approximately spherical), with a standard deviation as
   given. This may be used if scales are varying too wildly, particularly
   in the detector plane. The default is no restraints on scales. A tie
   is recommended (a) if scales are varied across the detector, eg TIE
   DETECTOR 0.1, or (b) for SECONDARY or SURFACE corrections, eg TIE
   SURFACE 0.001

   UNTIE may be used to remove the default restraints on SURFACE and A1
   (not recommended)

        SURFACE: tie surface parameters to spherical surface [default is
                TIE SURFACE 0.001]

        BFACTOR: tie Bfactors along rotation
        A1: tie TAILS parameter A1 to starting value, ie that given on
                the SCALES command [default is TIE A1 4]

        ROTATION: tie parameters along rotation axis (mainly useful with
                BATCH mode)

        DETECTOR: tie parameters on detector

  NORMALISE [SCALES|BFACTOR] [BEST|FIRST|RUN <run_number>]

   Controls which scale factors and Bfactors are "normalised", ie set to
   1.0 or 0.0. The overall scale of the data is indeterminate, so one
   scale factor needs to be set = 1.0: similarly, one relative B-factor
   needs to be set = 0.0. The default options are to normalise scales on
   the first part of the first run, and Bfactors on the best part (ie to
   make all the Bfactors negative: because of the smoothing they may
   still go slightly positive). The normalisation of the scales is not
   important, but the normalisation of Bfactors is, because negative Bs
   will sharpen data, while positive Bs will blur it.

        SCALES
                Following keywords apply to scales

        BFACTORS
                Following keywords apply to Bfactors [default]

        BEST
                Normalise B-factors on the best bit (not applicable to
                scales) [default for Bfactors]

        FIRST
                Normalise on the beginning of the first run [default for
                scales]

        RUN <run_number>
                Normalise on the beginning of the defined run

  OUTPUT <subkeywords>

   Control what goes in the output file. Three types of output MTZ file
   may be produced: (a) AVERAGE, average intensity for each hkl (I+ &
   I-). (b) SEPARATE, observations from input file with scale calculated,
   for re-input to Scala (or Postref, see POSTREF option) (c) UNMERGED,
   unaveraged observations, but with scales applied, partials summed or
   scaled, and outliers rejected.

   A reference batch is always excluded from the final statistics, even
   if it is included in the output file (only possible with the SEPARATE
   option).

   File format options:

        NONE
                no output file written

        AVERAGE
                [default] output averaged intensities, <I+> & <I-> for
                each hkl

        SEPARATE
                output observations as input, but with added columns for
                SCALE etc. This file may be reinput to Scala for further
                scaling (e.g. with a different scaling model)

        POSTREF
                append columns for Postref. This option implies SEPARATE.
                The added columns are IMEAN SIGIMEAN ISUM SIGISUM IMEAN
                mean of fully-recorded reflections ISUM summed partials
                (partials only)

        UNMERGED
                apply scales, sum or scale partials, reject outliers, but
                do not average observations

        POLISH
                Write reflections also to a formatted file as well as the
                MTZ file (logical name SCALEPACK) in some obscure format
                as written by "scalepack" (or my best approximation to
                it). Why would anyone want to do this? If the UNMERGED
                option is also selected, then the output matches the
                scalepack "output nomerge original index", otherwise it
                is the "normal" scalepack output, with either I, sigI or
                I+ sigI+, I-, sigI-, depending on the "anomalous" flag.

   Dataset options (only relevent for multiple datasets):

        SPLIT
                If there are multiple datasets defined, split them into
                separate output files [this is the default]. The base
                filename is taken from the HKLOUT, with the datasetname
                added for each dataset.

        TOGETHER
                NOT YET IMPLEMENTED. Write out multiple datasets into the
                same file, but labelled as different datasets

   Other options:

   (a) UNMERGED options:

        ORIGINAL
                write original indices hkl: M/ISYM = 1 for all
                reflections

        REDUCED
                [default] hkl indices are reduced to asymmetric unit, as
                in input file

        BEAMS
                output direction cosines of incident (s0) and diffracted
                (s2) beams in output file (columns S0X, S0Y, S0Z, S2X,
                S2Y, S2Z). These vectors are in the orthogonalised
                crystal frame with x,y,z axes along a*, c x a*, c

   (b) SEPARATE (POSTREF) options
          the following apply only to the SEPARATE (POSTREF) option, and
          must not precede that switch:-

        REFERENCE
                write reference batch (if present) to output file

        NOREFERENCE
                [default] omit reference batch (if present) from output
                file

        KEEP
                [default unless average] keep reflections outside
                resolution limits. The SCALE column will be set = 0.0

        KEEP SCALE
                keep reflections outside resolution limits, and calculate
                scales for them. This is dangerous unless the proportion
                of reflections omitted from scaling is small

        EXCLUDE
                [default if AVERAGE] exclude reflections outside
                resolution limits

        OMIT OUTLIERS
                omit rejected outliers from output file (SEPARATE &
                POSTREF options only). In this case a ROGUES file is
                written (see below) [default keep them in, but flagged in
                the FLAG column]

        OMIT PARTIALS [RUN <Nrun>]
                omit partially recorded reflections from output file. If
                no run number is given, then it applies to all runs.
                Multiple runs may specified on successive OUTPUT OMIT
                PARTIALS RUN commands

        ROGUES
                write a list of rejected reflections is written to the
                file ROGUES. This may be assigned on the command line. A
                ROGUES file is always written for the AVERAGE & UNMERGED
                options. [for SEPARATE, default no ROGUES file written
                unless OMIT OUTLIERS option used]

  FINAL [ NONE | FULLS | ONLYFULLS

          | SCALE_PARTIAL <Minimum_fraction>
          | PARTIALS [[NO]CHECK] | [NO]TEST [<lower_limit> <upper_limit>]
          [CORRECT <minimum_fraction>] [[NO]GAP] [MAXWIDTH
          <maximum_width>] ]

   Select whether or not to use summed or scaled partials in the final
   analysis after scale determination. If this command is missing, summed
   partials will be included if the input file contains a FRACTIONCALC
   column.

   Subkeys:

        NONE
                no final analysis/output pass

        FULLS
                use fulls only (& previously summed partials, eg from
                MOSFLM ADDPART or Scalepack) [default if no FRACTIONCALC
                column]

        ONLYFULLS
                use fulls only: exclude previously summed partials (from
                MOSFLM)

        SCALE_PARTIALS
                use scaled partials greater than <Minimum_fraction> in
                the merging. Only use this if the FRACTIONCALC column
                contains a good estimate of the partiality.

        PARTIALS
                use summed partials in final analysis (if present). See
                introduction above for a description of the use of
                partially recorded reflections. [this is the default if
                FRACTIONCALC column is present] The following flags are
                qualifiers of PARTIALS and will override those given on a
                previous PARTIALS command, for the merging step only (not
                scaling):

              [NO]CHECK
                      do [not] check for consistency of MPART flags (if
                      present). Reflections failing this test are tested
                      for total fraction (see TEST option) [default do if
                      MPART is present]

              [NO]TEST [<lower_limit> <upper_limit>]
                      do [not] accept partials only if total fraction
                      (from FRACTIONCALC column) is in range lower_limit
                      -> upper_limit [default if no MPART flag, limits
                      0.95, 1.05]

              CORRECT [<minimum_fraction>]
                      Scale partials in range minimum_fraction ->
                      lower_limit, predicted total fraction (needs
                      reliable FRACTIONCALC) [default minimum =
                      <lower_limit>]

              [NO]GAP
                      do [not] accept partials with a gap in, e.g. a
                      partial over 3 parts with the middle one missing.
                      GAP implies NOCHECK and TEST: CORRECT may also be
                      set. [default GAP]

              MAXWIDTH <maximum_width>
                      maximum number of parts for an acceptable summed
                      partial

  [UN]FIX [V] [A0] [A1]

   Option to fix or free TAILS parameters: by default V & A1 are free, A0
   is fixed [default A0 = 0.0]. Fixing A1 may help for low resolution
   data particularly.

  LINK [SURFACE|TAILS] ALL | <run_2> TO <run_1>

   run_2 will use the same SURFACE (or SECONDARY) or TAILS parameters as
   run_1. This can be useful when different runs come from the same
   crystal, and may stabilize the parameters. LINK TAILS ALL will use the
   same tails parameters for all runs for which TAILS parameters are
   refined. The keyword ALL will be assumed if omitted.
     * For TAILS parameters, the default is LINK TAILS ALL, but any LINK
       or UNLINK command will override this.
     * For SECONDARY or SURFACE parameters, the default is to link runs
       which come from the same dataset. They should be UNLINKed if they
       are different.

  UNLINK [SURFACE|TAILS] ALL | <run_2> TO <run_1>

   Remove links set by LINK command (or by default). The keyword ALL will
   be assumed if omitted, e.g. UNLINK TAILS [ALL] will use seperate tails
   parameters for each run.

  SKIP <N_skip> [[FOR] <N_skip_cycles>]

   Allow a subset of reflections to be used during the initial cycles of
   scaling, to speed up the program. For the first N_skip_cycles, only
   every N_skip'th unique reflection will be used. N_skip_cycles defaults
   = Ncycle-2, and the program will force 2 more cycles with all data if
   convergence is reached while reflections are still being skipped. You
   should check that convergence has been reached with all observations,
   particularly if the number of observations used in the early cycles is
   small.

  FILTER <Filter> [<Damp>]

   Define filter level, & damp level. In the minimization, shifts
   corresponding to eigenvalues .lt. <Filter> are removed, <Damp> is
   added to all eigenvalues. [Default 1.0e-6, 0.0]

  DAMP [NONE] | <Damp> <NcycDamp>

   Set damping level for shifts. <Damp> is added to all eigenvalues for
   the first <NcycDamp> cycles. This may be useful if the scales vary
   over a wide range, particularly if the scale refinement diverges at
   first, but is not normally recommended, as it seems to slow
   convergence. Default is DAMP NONE. If <NcycDamp> is omitted, the
   damping applies to all cycles

  BINS <Nsrange>

   Define number of resolution bins for analysis [default 10]

  XYBINS <Nx> [<Ny>]

   Define number of bins across detector, x (=XDET) and y (YDET). Only
   used if XDET, YDET columns are present in input file <Ny> defaults to
   <Nx>. XYBINS 0 turns off analysis [default Nx = Ny = 20]

  SMOOTHING <subkeyword> <value>

   Set smoothing factors ("variances" of weights). A larger "variance"
   leads to greater smoothing

   Subkeys:

        TIME <Vt>
                smoothing of B-factors [default 0.5]

        ROTATION <Vz>
                smoothing of scale along rotation [default 1.0]

        DETECTOR <Vxy>
                smoothing of scale on detector [default 1.0]

        PROB_LIMIT <DelMax_t> <DelMax_z> <DelMax_xy>
                maximum values of normalized squared deviation (del**2/V)
                to include a scale [default set automatically, typically
                3.0]

  INSCALE OFF | ON

   Switch OFF or ON application of an input SCALE column. By default, if
   the input file contains a column called SCALE (e.g. from a previous
   run of Scala), it will be applied.

  NOSCALE

   Don't do any scaling, just the final analysis (equivalent to CYCLES 0)

  DUMP [<Scale_file_name>]

   Dump all scale factors to a file after each cycle. These can be used
   to restart scaling using the RESTORE option, or for rerunning the
   merge step. If no filename is given, the scales will be written to
   logical file SCALES, which may be assigned on the command line. DUMP
   is set by default, but may be turned off with the NODUMP command.

  NODUMP

   No dump of scales to file. Default is DUMP.

  ANALYSE [[NO]NORMAL] [[NO]PLOT] [MAXDENSITY <maximum point density>]

   This command controls the normal probability analyses

   Subkeys:

        [NO]NORMAL
                do [not] do normal probability analyses [default do them]

        [NO]PLOT
                do [not] write normal probability plot to output file
                with logical name DELTA [default do write file]. This
                file contains pairs of delta(expected), delta(observed)
                for fulls, then summed partials, then scaled partials

        MAXDENSITY
                maximum point density for normal probability plot. This
                plot includes a point for every observation, so in large
                datasets it can get very big. This parameter allows the
                sampling of the plot, so that in the central crowded part
                only some of the points are included in the plotfile
                [default 25]

  HISTORY <history line>

   Define optional line to be added to the history records in the file.
   This is in addition to a line giving the date and time of the run,
   which is always added. Only one optional history line may be added.

  OVERLAPMAP

   Write the overlap matrix from the initial analysis to a map file
   assigned to MAPOUT. Note that the initial analysis is not done if the
   RESTORE option is used or INITIAL NONE is set.

  WIDTH WILSON | LINEAR | SQUARE [<mid-point>]

   Select binning mode on intensity

   Subkeys:

        WILSON
                [default] exponential bins

        LINEAR
                linear bins

        SQUARE
                quadratic bins

   In each case, <mid-point> is the limit for the middle bin.

  NAME [RUN <RunNumber(s)>] PROJECT <project_name> CRYSTAL <crystal_name>
  DATASET <dataset_name>

   Assign or reassign project/crystal/dataset names, for output file. The
   names given here supersede those in the input file.

   If the RUN subkey is present, different runs (or groups of runs) may
   be assigned to different datasets. If the RUN subkey is omitted, the
   names apply to all data. RunNumber may be a list or a range of run
   numbers (see examples below). DATASET must be present: if PROJECT or
   CRYSTAL are omitted, they take the value last given for these
   parameters. DATASET may optionally be given in the syntax
   crystal_name/dataset_name

   Examples:
name run 1      project  Lysozyme crystal  Native dataset L1
name run 2 3         dataset  L2  #  takes project & crystal from previous line
name run 4 to 6    crystal Native  dataset L3

  BASE [CRYSTAL <crystal_name>] DATASET <base_dataset_name>

   If there are multiple datasets in the input file, define the "base"
   dataset for analysis of dispersive (isomorphous) differences.
   Differences between other datasets and the base dataset are analysed
   for correlation and ratios, ie for the i'th dataset (I(i) - I(base)).
   By default, the datasets with the shortest wavelength will be chosen
   as the base (or dataset 1 if wavelength is unknown). Typically, the
   CRYSTAL keyword may be omitted.

  PNAME <project_name>

   OBSOLETE keyword: use NAME instead.
   Project Name. In most cases, this will be inherited from the MTZ file.
   A dataset, as listed in the MTZ header, is specified by a
   project-name/dataset-name pair. The project-name specifies a
   particular structure solution project, while the dataset-name
   specifies a particular dataset contributing to the structure solution.
   An entry in the PNAME keyword should therefore be accompanied by a
   corresponding entry in the DNAME keyword.

  DNAME <dataset_name>

   OBSOLETE keyword: use NAME instead.
   Dataset Name. In most cases, this will be inherited from the MTZ file.
   A dataset, as listed in the MTZ header, is specified by a
   project-name/dataset-name pair. The project-name specifies a
   particular structure solution project, while the dataset-name
   specifies a particular dataset contributing to the structure solution.
   An entry in the DNAME keyword should therefore be accompanied by a
   corresponding entry in the PNAME keyword.

  PRIVATE

   Set the directory permissions to '700', i.e. read/write/execute for
   the user only (default '755').

  USECWD

   Write the deposit file to the current directory, rather than a
   subdirectory of $HARVESTHOME. This can be used to send deposit files
   from speculative runs to the local directory rather than the official
   project directory, or can be used when the program is being run on a
   machine without access to the directory $HARVESTHOME.

  RSIZE <row_length>

   Maximum width of a row in the deposit file (default 80). <row_length>
   should be between 80 and 132 characters.

  NOHARVEST

   Do not write out a deposit file; default is to do so provided Project
   and Dataset names are available.

                           INPUT AND OUTPUT FILES

  Input

   HKLIN
          The input file must be sorted on H K L M/ISYM BATCH
          Compulsory columns:
        H K L           indices
        M/ISYM          partial flag, symmetry number
        BATCH           batch number
        I               intensity  (integrated intensity)
        SIGI            sd(intensity)   (integrated intensity)
          Optional columns:
        XDET YDET       position on detector of this reflection: these
                        may be in any units (e.g. mm or pixels), but the
                        range of values must be specified in the
                        orientation data block for each batch. If
                        these columns are absent, the scale may not be
                        varied across the detector (i.e. only SCALES
                        DETECTOR 1 is valid)
        ROT             rotation angle of this reflection ("Phi"). If
                        this column is absent, only SCALES BATCH is valid.
        IPR             intensity  (profile-fitted intensity)
        SIGIPR          sd(intensity)   (profile-fitted intensity)
        SCALE           previously calculated scale factor (e.g. from
                        previous run of Scala). This will be applied
                        on input
        SIGSCALE        sd(SCALE)
        TIME            time for B-factor variation (if this is
                        missing, ROT is used instead)
        MPART           partial flag from Mosflm
        FRACTIONCALC    calculated fraction, required to SCALE PARTIALS
        LP              Lorentz/polarization correction (already applied)
        FLAG            error flag (packed bits)
                        for now, pending proper implementation, if this column
                        is present, observations with a  non-zero FLAG will be
                        unconditionally omitted

  Output

   HKLOUT

        (a) Option AVERAGE
                The output file contains columns

H K L  IMEAN SIGIMEAN  I(+) SIGI(+)  I(-) SIGI(-)

                Note that there are no M/ISYM or BATCH columns. I(+) &
                I(-) are the means of the Bijvoet positive and negative
                reflections respectively and are always present even for
                the option ANOMALOUS OFF.

        (b) Option SEPARATE
                The output file contains the same columns as the input,
                with some columns added if not previously present:-

                SCALE & SIGSCALE - the calculated scale factor & its sd
                (this may be applied in another run of Scala). SCALE will
                be = 0.0 for reflections outside the resolution cutoff,
                if they are included in the output file (option OUTPUT
                KEEP) (see example)

                SIGIC [, SIGIPRC] - the corrected standard deviations of
                I [and IPR], as altered by SDCORR commands. These columns
                are only written if a SDCORRECTION command is given to
                Scala.

                If the OUTPUT POSTREF option is given, then also the
                columns IMEAN SIGIMEAN ISUM SIGISUM are added

        IMEAN    mean of fully-recorded reflections
        ISUM     summed partials (partials only)

        (c) Option UNMERGED
                As for SEPARATE, but with scales applied, with no
                partials (i.e. partials have been summed or scaled,
                unmatched partials removed), & outliers rejected. If a
                separate profile-fitted intensity column IPR, SIGIPR is
                present in the input file as well as columns I, SIGI,
                only one set will be chosen, as specified. Columns
                defining the diffraction geometry (e.g. XDET YDET ROT
                TIME LP FRACTIONCALC) will be preserved in the output
                file.

                Output columns:

        H,K,L     REDUCED or ORIGINAL indices (see OUTPUT options)
        M/ISYM    Symmetry number (REDUCED), = 1 for ORIGINAL indices
        BATCH     batch number as for input
        I, SIGI   scaled intensity & sd(I)
        SCALE     scale factor applied
        SIGSCALE  sd(SCALE)
        NPART     number of parts, = 1 for fulls, negated for scaled
                   partials, i.e. = -1 for scaled single part partial
        TIME      copied from input if present
        XDET,YDET copied from input if present
        ROT       copied from input if present (averaged for
                    multi-part partials)
        FRACTIONCALC total fraction (if present in input file)
        LP        copied from input if present
   If BEAM option is used:-
        S0X, S0Y, S0Z  direction cosines of incident beam in
                  orthogonalised crystal frame ( x,y,z axes along
                  a*, c x a*, c)
        S2X, S2Y, S2Z  direction cosines of diffracted beam in
                  orthogonalised crystal frame

   SCALES
          scale factors from DUMP, used by RESTORE option
   ROGUES
          list of bad agreements
   PLOT
          If SCALES SECONDARY or SURFACE options are used, graph of
          correction surface (Plot84 format)
   NORMPLOT
          normal probability plot from merge stage
          *** this is at present written is a format for plotting program
          xmgr ***
   ANOMPLOT
          normal probability plot of anomalous differences
            (I+ - I-)/sqrt[sd(I+)**2 + sd(I-)**2]
          *** this is at present written is a format for plotting program
          xmgr ***
   SCALEPACK
          Formatted output selected by the command OUTPUT POLISH
     _________________________________________________________________

EXAMPLES

    1. Simple smoothed scaling, with some alternatives flagged as #*#
set crystal = "tfn2"
scala hklin     ${crystal}_srs  \
      hklout    ${crystal}_merge \
      scales    ${crystal}_${run}.scales \
      rogues    ${crystal}_${run}.rogues \
      normplot  ${crystal}_${run}.norm \
            << eof

run  1 all

intensities partial     # we have few fulls: this is the default

cycles 20

anomalous off           # this is a native set
#*# anomalous on        #   or a derivative

sdcorrection 1.3 0.02   # from a previous run

# try it with and without the tails correction: this is with tails
scales   rotation spacing 10  bfactor on    tails
#*#
#*#  Some alternatives
#*# >> Recommended usual case
#*# scales rotation spacing 5 secondary 6 bfactor off tails
#*#
#*# >> If you have radiation damage, you need a Bfactor,
#*# >>  but a Bfactor at coarser intervals is more stable
#*# scales  rotation spacing 5 secondary 6  tails \
#*#    bfactor on brotation spacing 20
#*# tie bfactor 0.5     ##  restarining the Bfactor also helps
#*#


reject 4              # reject outliers more than 4sd from mean
#*# reject 6 all 8  is default

exclude emax 8        # reject very large observations
                      #    default is Emax 10

eof
    2. Simple Batch scaling
#!/bin/csh -f
#
# Scale data from Mosflm, merge with Scala
#
scala hklin jpa_example hklout jpa_example_sc \
      scales   jpa.scales \
      rogues   jpa.rogues \
      normplot jpa.norm \
      anomplot jpa.anom \
<< eof-1
run 1 batch 2001 to 2049
run 2 batch 2051 to 2100
cycles 8
sdcorr  1.5  0.03
scales batch  bfactor on    # batch scaling is generally poorer than smoothed
reject merge 4
anomalous on
eof-1
    3. A more complicated example, smooth scaling of native, then scaling
       of derivative to native
#!/bin/csh -f
#
#scala
#
cd /scr0/fm1/Temp
#
##
#==== Sort native output from Mosflm together
##
sort:
sortmtz hklout m6c8_sort.mtz  << end_sort
H K L M/ISYM BATCH I SIGI
m6c8a1.mtz
m6c8a2.mtz
end_sort
#
##
#==== scale native data together, no Bfactor, smooth scale on rotation
#==== merge native
##
scala hklin m6c8_sort.mtz hklout m6c8_scala <<EOF
run 1 batch 1 to 90000
title frozen native monoclinic m6c8
scales bfactor off  rotation spacing 5
resolution 25 6.1
anomalous off
reject merge  4
sdcorr  1.3  0.04
EOF
#
# Convert native data into form suitable for reinput to Scala
combat  hklin m6c8_scala hklout m6c8_r << eof-r
input mtzi
labin I=IMEAN SIGI=SIGIMEAN
batch 1
eof-r
#
##
#==== Sort derivative data together
##
sort:
sortmtz hklout m6cb3_sort.mtz  << end_sort
H K L M/ISYM BATCH I SIGI
m6cb3b.mtz
m6cb3c.mtz
end_sort
#
##
#==== Combine together merged native & sorted derivative data, by
#     interleaving reflection records
#     Must resort data after this step
##
mtzutils:
mtzutils hklin2 m6cb3_sort.mtz \
         hklin1 m6c8_r \
         hklout temp_m6cb3_resort << eof-m
merge
eof-m
#
sortmtz hklin temp_m6cb3_resort hklout m6cb3_resort << eof-m
H K L M/ISYM BATCH
eof-m
#
##
#==== Scale and merge derivative data, using native data as reference (run 1)
#     Use secondary beam absorption correction for derivative,
#       but with some restraints (tie)
#     The reference data (native) is omitted from the output file
##
scala hklin m6cb3_resort.mtz hklout m6cb3_scala \
  scales    m6cb3.scales \
  rogues    m6cb3.rogues \
  normplot  m6cb3.norm   \
  anomplot  m6cb3.anom   \
  plot      m6cb3.plt    \
 <<EOF
run 1 batch 1 reference
run 2 batches 10 to 23156 exclude 23152          #  reject one duff batch
run 3 batches 23157 to 90000
title frozen native monoclinic m6cb3
scales bfactor off  rotation spacing 5 secondary 6
tie surface 0.001  # this is the defeult value anyway
resolution 25 2.5
reject merge  4
anomalous on
sdcorr  1.1  0.005
EOF
#
#
#
#exit
trunc:
truncate  hklin  m6cb3_scala \
          hklout /ss3/fm1/Mutase/Derivs_FzM/m6cb3_F <<end-trunc
anomalous yes
resolution  25 2.5
nresidue   1400
labout  F=FM623 SIGF=SIGFM623 DANO=DANOM623 SIGDANO=SIGDANOM623
end-trunc
    4. Scaling of several MAD datasets together, no reference dataset
#!/bin/csh -f

# Define a base name for files created in this script
set name = dfxe_3d
set project = dfxe
set crystal = crys1

# Input filenames for the 4 datasets at different wavelengths
set l1 = dfxe_1   # peak
set l2 = dfxe_2   # inflection
set l3 = dfxe_3   # hard remote
set l4 = dfxe_4   # 1A wavelength

set nl1 = peak
set nl2 = inflect
set nl3 = highE
set nl4 = lowE

# Angular spacing for smoothed scales
set spacing = 5

# Sort together the initial data files
sortmtz hklout ${name}_all << eof-s
H K L M/ISYM BATCH
${l1}.mtz
${l2}.mtz
${l3}.mtz
${l4}.mtz
eof-s


###=== Step 1 ==========================================================
###===    Scale all datasets together
###===    This will write out 4 output files, with filenames constructed
###===    by appending the dataset name on to the hklout name
scale_1:
set run = all
scala hklin ${name}_all  hklout ${name} \
      scales   ${run}.scales \
      normplot ${run}.norm \
      anomplot ${run}.anom \
      rogues   ${run}.rogues \
                                      << eof-r1
title Scale all datasets together, smooth, secondary
#  Define runs
run 1 batch 1000 to 1999
run 2 batch 2000 to 2999
run 3 batch 3000 to 3999
run 4 batch 4000 to 4999

#  Define datasets: this should have been done in Mosflm previously
name  run 1   project ${project} crystal ${crystal} dataset ${nl1} # peak
name  run 2   project ${project} crystal ${crystal} dataset ${nl2} # inflection
name  run 3   project ${project} crystal ${crystal} dataset ${nl3} # highE
name  run 4   project ${project} crystal ${crystal} dataset ${nl4} # lowE

# Dispersive differences for analysis are relative to the "base" dataset
base dataset highE


# If using secondary beam correction, usually turn Bfactor off
# unless you have high resolution and radiation damage

scales rotation spacing ${spacing}  bfactor off secondary 6
tie surface 0.001    # this is the default restraint to keep the
                     # absorption surface spherical

anomalous on

# reject on 5 sigma within the I+ or I- sets, 8 sigma between I+ & I-
reject 5 all 8

eof-r1

eof-${run}

###===   Convert I to F, do Wilson plot, for each dataset
###===   A future change to Truncate may allow processing of multiple
###===   datasets together
l1:
set ln = ${nl1}
truncate hklin ${name}_${ln} hklout ${name}_${ln}_f << eof_t${ln}
nresidues 117
ranges 30
labout F=F${ln} SIGF=SIGF${ln} \
   DANO=DANO${ln}  SIGDANO=SIGDANO${ln}  ISYM=ISYM${ln} \
   F(+)=F${ln}(+) SIGF(+)=SIGF${ln}(+)  F(-)=F${ln}(-) SIGF(-)=SIGF${ln}(-)
eof_t${ln}

l2:
set ln = ${nl2}
truncate hklin ${name}_${ln} hklout ${name}_${ln}_f << eof_t${ln}
nresidues 117
ranges 30
labout F=F${ln} SIGF=SIGF${ln} \
   DANO=DANO${ln}  SIGDANO=SIGDANO${ln}  ISYM=ISYM${ln} \
   F(+)=F${ln}(+) SIGF(+)=SIGF${ln}(+)  F(-)=F${ln}(-) SIGF(-)=SIGF${ln}(-)
eof_t${ln}

l3:
set ln = ${nl3}
truncate hklin ${name}_${ln} hklout ${name}_${ln}_f << eof_t${ln}
nresidues 117
ranges 30
labout F=F${ln} SIGF=SIGF${ln} \
   DANO=DANO${ln}  SIGDANO=SIGDANO${ln}  ISYM=ISYM${ln} \
   F(+)=F${ln}(+) SIGF(+)=SIGF${ln}(+)  F(-)=F${ln}(-) SIGF(-)=SIGF${ln}(-)
eof_t${ln}

l4:
set ln = ${nl4}
truncate hklin ${name}_${ln} hklout ${name}_${ln}_f << eof_t${ln}
nresidues 117
ranges 30
labout F=F${ln} SIGF=SIGF${ln} \
   DANO=DANO${ln}  SIGDANO=SIGDANO${ln}  ISYM=ISYM${ln} \
   F(+)=F${ln}(+) SIGF(+)=SIGF${ln}(+)  F(-)=F${ln}(-) SIGF(-)=SIGF${ln}(-)
eof_t${ln}

###===   Sort together merged data for all wavelength, outputting a
###===   single record for each hkl
###===   For each wavelength, store amplitude F & sigF,
###===   anomalous difference DANO (= F+ - F-) & sigDANO,
###===   and ISYM flag which shows if both F+ & F- were measured
cad  hklout ${name}_fcad  \
     hklin1 ${name}_${nl1}_f \
     hklin2 ${name}_${nl2}_f \
     hklin3 ${name}_${nl3}_f \
     hklin4 ${name}_${nl4}_f       << eof-c
labin  file_number 1  \
  E1=F${nl1} E2=SIGF${nl1} E3=DANO${nl1} E4=SIGDANO${nl1} E5=ISYM${nl1} \
  E6=F${nl1}(+) E7=SIGF${nl1}(+) E8=F${nl1}(-) E9=SIGF${nl1}(-)
labin  file_number 2  \
  E1=F${nl2} E2=SIGF${nl2} E3=DANO${nl2} E4=SIGDANO${nl2} E5=ISYM${nl2} \
  E6=F${nl2}(+) E7=SIGF${nl2}(+) E8=F${nl2}(-) E9=SIGF${nl2}(-)
labin  file_number 3  \
  E1=F${nl3} E2=SIGF${nl3} E3=DANO${nl3} E4=SIGDANO${nl3} E5=ISYM${nl3} \
  E6=F${nl3}(+) E7=SIGF${nl3}(+) E8=F${nl3}(-) E9=SIGF${nl3}(-)
labin  file_number 4  \
  E1=F${nl4} E2=SIGF${nl4} E3=DANO${nl4} E4=SIGDANO${nl4} E5=ISYM${nl4} \
  E6=F${nl4}(+) E7=SIGF${nl4}(+) E8=F${nl4}(-) E9=SIGF${nl4}(-)
eof-c
     _________________________________________________________________

REFERENCES

    1. W. Kabsch, J.Appl.Cryst. 21, 916-924 (1988)
    2. P.R.Evans, "Data reduction", Proceedings of CCP4 Study Weekend,
       1993, on Data Collection & Processing, pages 114-122
    3. P.R.Evans, "Scaling of MAD Data", Proceedings of CCP4 Study
       Weekend, 1997, on Recent Advances in Phasing, Click here
    4. R.Read, "Outlier rejection", Proceedings of CCP4 Study Weekend,
       1999, on Data Collection & Processing
    5. Hamilton, Rollett & Sparks, Acta Cryst. 18, 129-130 (1965)
    6. Blessing, R.H., Acta Cryst. A51, 33-38 (1995)
    7. Kay Diederichs & P. Andrew Karplus,"Improved R-factors for
       diffraction data analysis in macromolecular crystallography",
       Nature Structural Biology, 4, 269-275 (1997)
    8. Manfred Weiss & Rolf Hilgenfeld, "On the use of the merging R
       factor as a quality indicator for X-ray data", J.Appl.Cryst. 30,
       203-205 (1997)
    9. Manfred Weiss, "Global Indicators of X-ray data quality"
       J.Appl.Cryst. 34, 130-135 (2001)
     _________________________________________________________________

Appendix 1: Partially recorded reflections

   Partially recorded reflections may optionally be used in scaling
   (controlled by the command INTENSITIES), and in the final analysis
   (controlled by the command FINAL). The default is to include summed
   partials in both scaling and the final analysis and merging.

   Different options for the treatment of partials are set for both
   scaling & merging stages by the PARTIALS command, or separately for
   the scaling stage (INTENSITIES command) and the merging stage (FINAL
   command). Partials may either be summed (subkeyword PARTIALS, with
   various options), or scaled (subkeyword SCALE_PARTIALS): in the latter
   case, each part is treated independently of the others. If summed
   partials are used in scaling with the SCALES BATCH option, the
   FRACTIONCALC is used to partition the effects of the different scales
   for the two halves. In the input file, partials are flagged with M=1
   in the M/ISYM column, and have a calculated fraction in the
   FRACTIONCALC column. Data from Mosflm also has a column MPART which
   enumerates each part (e.g. for a reflection predicted to run over 3
   images, the 3 parts are labelled 31, 32, 33), allowing a check that
   all parts have been found: MPART = 10 for partials already summed in
   MOSFLM.

   For datasets with few partials, with low mosaicity compared to the
   image widths, very few partials run over more than two images, &
   partial summation is not usually a problem. If you have many partials
   running over 3 or more images, you may need to tune the partial
   selection flags below to accept or reject partial sets according to
   their reliability.

   Summed partials:
   All the parts are summed (after applying scales) to give the total
   intensity, provided some checks are passed. The options to use
   partials as well as fulls are defined separately for the scaling and
   merging steps on the INTENSITIES and FINAL commands. The parameters
   for the checks are set by the PARTIALS command for both stages, or
   separately on the INTENSITIES and FINAL commands. The number of
   reflections failing the checks is printed. You should make sure that
   you are not losing too many reflections in these checks.
   (a)
          At least two parts must be present (unless the CORRECT option
          is set, see (e) below)
   (b)
          not more than MAXWIDTH <maximum_width> parts must be present
          [default maximum_width = 5]
   (c)
          if the CHECK option is set (the default if an MPART column is
          present), the MPART flags are examined. If they are consistent,
          the summed intensity is accepted. If they are inconsistent
          (quite common), the total fraction is checked unless NOTEST is
          specified, in which case they are rejected. NOCHECK switches
          off this check.
   (d)
          if the TEST option is set (default if no MPART column), the
          summed reflection is accepted if the total fraction (the sum of
          the FRACTIONCALC values) lies between <lower_limit> ->
          <upper_limit> [default limits = 0.95 1.2]
   (e)
          if the CORRECT option is set, the total intensity is scaled by
          the inverse total fraction for total fractions between
          <minimum_fraction> to <lower_limit>. This works also for a
          single unmatched partial. As for the scaled partial option,
          this correction relies on accurate FRACTIONCALC values, so
          beware.
   (f)
          if the GAP option is set, partials with a gap in are accepted,
          e.g. a partial over 3 parts with the middle one missing. The
          GAP option implies TEST & NOCHECK, & the CORRECT option may
          also be set.

   By setting the TEST & CORRECT limits, you can control summation &
   scaling of partials, e.g .
      TEST 1.2 1.2 CORRECT 0.5

   will scale up all partials with a total fraction between 0.5 & 1.2
      TEST 0.95 1.05

   will accept summed partials 0.95->1.05, no scaling
      TEST 0.95 1.05 CORRECT 0.4

   will accept summed partials 0.95->1.05, and scale up those with
   fractions between 0.4 & 0.95

   Note that a profile-fitted intensity, if present in the file as a
   separate IPR column, will not be used for a scaled partial, unless the
   PARTIALS USE_PROFILE flag is set.

   Scaled partials:
   In this option, each individual partial observation scaled up by the
   inverse FRACTIONCALC, provided that the fraction is greater than
   <minimum_fraction> [default = 0.5].
     _________________________________________________________________

Appendix 2: Scaling algorithm

   For each reflection h, we have a number of observations Ihl, with
   estimated standard deviation shl, which defines a weight whl. We need
   to determine the inverse scale factor ghl to put each observation on a
   common scale (as Ihl/ghl). This is done by minimizing

        Sum( whl * ( Ihl - ghl * Ih )**2 )   Ref Hamilton, Rollett & Sparks

   where Ih is the current best estimate of the "true" intensity
        Ih = Sum ( whl * ghl * Ihl ) / Sum ( whl * ghl**2)

   Each observation is assigned to a "run", which corresponds to a set of
   scale factors. A run would typically consist of a continuous rotation
   of a crystal about a single axis.

   The inverse scale factor ghl is derived as follows:
        ghl = Thl * Chl * Shl

   where Thl is an optional relative B-factor contribution, Chl is a
   scale factor (1-dimensional or 3-dimensional (ie DETECTOR option)),
   and Shl is a anisotropic correction expressed as spherical harmonics
   (ie SECONDARY or SURFACE options).

   a) B-factor (optional)

   For each run, a relative B-factor (Bi) is determined at intervals in
   "time" ("time" is normally defined as rotation angle if no independent
   time value is available), at positions ti (t1, t2, . . tn). Then for
   an observation measured at time tl
        B = Sum[i=1,n] ( p(delt) Bi ) / Sum (p(delt))

        where   Bi  are the B-factors at time ti
                delt    = tl - ti
                p(delt) = exp ( - (delt)**2 / Vt )
                Vt  is "variance" of weight, & controls the smoothness
                        of interpolation

        Thl = exp ( + 2 s B )
                s = (sin theta / lambda)**2

   An alternative anisotropic B-factor may be used to correct for
   anisotropic fall-off of scattering: THIS OPTION IS NOT RECOMMENDED.
   This is parameterized on the components of the scattering vector
   (divided by 2 for compatibility with the normal definition of B) in
   two directions perpendicular to the Xray beam (y & z in the
   "Cambridge" coordinate frame with x along the beam).
        Thl = exp ( + 2[uy**2 Byy + 2 uy uz Byz + uz**2 Bzz])

        where  uy, uz are the components of d*/2

   Byy, Byz, Bzz are functions of time ti or batch as for the isotropic
   Bfactor. The principle components of B (Bfac_min, Bfac_max) are also
   printed.

   b) Scale factors

   For each run, scale factors Cxyz are determined at positions (x,y) on
   the detector, at intervals on rotation angle z. Then for an
   observation at position (x0, y0, z0),
        Chl(x0, y0, z0) =
   Sum(z)[p(delz){Sum(xy)[q(delxy)*Cxyz]/Sum(xy)[q(delxy)]}/Sum(z)[p(delz)]

where   delz    = z - z0
        p(delz) = exp(-delz**2/Vz)
        q(delxy)= exp(-((x-x0)**2 + (y-y0)**2)/Vxy)
        Vz, Vxy are the "variances" of the weight & control the smoothness
                of interpolation

   For the SCALES BATCH option, the scale along z is discontinuous: the
   normal option has one scale factor (or set of scale factors across the
   detector) for each batch. The SLOPE (not recommended) option has two
   scale factors per batch, with the scale interpolated linearly between
   the beginning and end according to the rotation angle of the
   reflection.

   c) Anisotropy factor

   The optional surface or anisotropy factor Shl is expressed as a sum of
   spherical harmonic terms as a function of the direction of
   (1) the secondary beam (SECONDARY correction) in the camera spindle
   frame,
   (2) the secondary beam (ABSORPTION correction) in the crystal frame,
   permuted to put either a*, b* or c* along the spherical polar axis
   or
   (3) the scattering vector in the crystal frame (SURFACE option).
    1. SECONDARY beam direction (camera frame)
         s  =  [Phi] [UB] h
         s2 = s - s0
         s2' = [-Phi] s2
Polar coordinates:
         s2' = (x y z)
         PolarTheta = arctan(sqrt(x**2 + y**2)/z)
         PolarPhi   = arctan(y/x)

                             where [Phi] is the spindle rotation matrix
                                   [-Phi] is its inverse
                                   [UB]  is the setting matrix
                                   h = (h k l)
    2. ABSORPTION: Secondary beam direction (permuted crystal frame)
         s    = [Phi] [UB] h
         s2   = s - s0
         s2c' = [-Q] [-U] [-Phi] s2
Polar coordinates:
         s2' = (x y z)
         PolarTheta = arctan(sqrt(x**2 + y**2)/z)
         PolarPhi   = arctan(y/x)

                             where [Phi] is the spindle rotation matrix
                                   [-Phi] is its inverse
                                   [Q] is a permutation matrix to put
                                       h, k, or l along z (see POLE option)
                                   [U]  is the orientation matrix
                                   [B]  is the orthogonalization matrix
                                   h = (h k l)
    3. Scattering vector in crystal frame
        (x y z) = [Q][B] h
Polar coordinates:
         PolarTheta = arctan(sqrt(x**2 + y**2)/z)
         PolarPhi   = arctan(y/x)

                             where [Q] is a permutation matrix to put
                                       h, k, or l along z (see POLE option)
                                   [B]  is the orthogonalization matrix
                                   h = (h k l)

   then
 Shl = 1  +  Sum[l=1,lmax] Sum[m=-l,+l] Clm  Ylm(PolarTheta,PolarPhi)

                             where Ylm is the spherical harmonic function for
                                       the direction given by the polar angles
                                   Clm are the coefficients determined by
                                       the program

   Notes:
     * The initial term "1" is essentially the l = 0 term, but with a
       fixed coefficient.
     * The number of terms = (lmax + 1)**2 - 1
     * Even terms (ie l even) are centrosymmetric, odd terms
       antisymmetric
     * Restraining all terms to zero (with the TIE SURFACE) reduces the
       anisotropic correction. This should always be done
     _________________________________________________________________

Appendix 3: TAILS correction

   For many crystals, the reflection profile on rotation ("phi") is not a
   simple closed curve, but has long tails due at least in part to
   thermal diffuse scattering (TDS): the amount of this depends on the
   crystal, and is larger at high resolution than at low resolution. If
   all reflections were scanned through the same angle, then equal
   amounts of this diffuse scattering would be included in each
   reflection. However, in typical "coarse sliced" data collection
   schemes, where the image rotation width is larger than the reflection
   width, reflections are recorded on a variable number of images, 1, 2,
   3 etc, and different amounts of the tails are included in the
   integrated intensity. This generally leads to a negative "partial
   bias", increasing with resolution, i.e. the apparent intensities of
   partially recorded reflections are higher than equivalent fulls.

   The TAILS correction is an attempt to correct for the different
   truncation of tails, by using a simple (crude) model of thermal
   diffuse scattering, although the correction only attempts to correct
   for the different truncation, and does not attempt to correct for
   diffuse scattering itself.

   Some of the ideas used are based on suggestions by R.H.Blessing,
   Cryst. Reviews, 1, 3-58 (1987), but he should not be blamed for this.

   This is a brief account of method (see code & comments in subroutine
   dffscn for more details):-
    1. I = J ( 1 + alpha)
       where J is the Bragg intensity (true intensity) & I is the
       measured intensity, i.e. the TDS intensity is proportional to the
       Bragg intensity
    2. alpha = alpha0 + alpha1 * (sin theta / lambda)**2
       where alpha0 & alpha1 are refinable parameters. This is a simple
       linear isotropic model to the amount of TDS. alpha0 should be 0.0,
       and may be fixed as such, but allowing it to vary seems to help
       sometimes. Both alpha0 & alpha1 are reset if they go negative in
       the refinement. An extension of the model would be to make alpha
       anisotropic.
    3. each reflection is scanned over an angle DPhi, which is an
       integral multiple of the image width (Dphi = Nimages * DelPhi). A
       rotation by DPhi moves the reflection a distance in reciprocal
       space
        Dq = Dphi * xsi,
       where xsi is the radius from the rotation axis
       If the half width of the reflection (including tails) is v
       (another refineable parameter), and 2v > Dq, then part of the
       tails will be truncated.
       Taking a simple model of the shape of the tails as a triangle of
       base width 2v, height in the middle h (h = J * alpha / v), then
       the area in the tails (= tail intensity) and the intensity
       truncated by the restricted scan range can be calculated. Then the
       corrected ("true") intensity J can be calculated
       For full scan:
        J = I / (1 + alpha)
       For truncated scan (missing parts of tails C1 & C2)
        J = I / (1 + alpha*(1 - C1 - C2))
    4. because this model is very crude, it seems insufficiently
       trustworthy to use as a proper correction for TDS. It does however
       seem reasonable to correct for the different amounts of tails
       truncation, C1 & C2 ( >= 0.0)
       The correction applied is thus
        I' = I * (1 + alpha) / (1 + alpha*(1 - C1 - C2))
    5. the parameters refined are v, alpha0 (A0) and alpha1 (A1). By
       default, the same parameters are used for all runs (see LINK,
       UNLINK). refinement of the parameters seems often to be unstable.
       If they are being reset from negative values, try setting A0 = 0.0
       (e.g. SCALES . . TAILS 0.005 0.0 30.0) and fixing A0 (FIX A0, this
       is the default)
     _________________________________________________________________

Appendix 4: Data from Denzo

   DENZO is often run refining the cell and orentation angles for each
   image independently, then postrefinement is done in Scalepack. It is
   essential that you do this postrefinement. Either then reintegrate the
   images with the cell parameters fixed, or use unmerged output from
   scalepack as input to Scala. The DENZO or SCALEPACK outputs will need
   to be converted to a multi-record MTZ file using COMBAT (see COMBAT
   documentation).

   Both of these options have some problems
     * If you take the output from Denzo into Scala, there may be
       problems with partially recorded reflections: it is difficult for
       Scala to determine reliably that it has all parts of a partial to
       sum together.
     * If you take unmerged output from scalepack into Scala, most of the
       geometrical information about how the observations were collected
       is lost, so many of the scaling options in Scala are not
       available. Only Batch scaling can be used, but simultaneous
       scaling of several wavelengths or derivatives may still be useful
     _________________________________________________________________

Appendix 5: Outlier algorithm

   The test for outliers is as follows:
   (1)
          if there are 2 observations (left), then
        (a)
               for each observation Ihl, test deviation
        Delta(hl) = |Chi|
         |Ihl - ghl Iother| / sqrt[sigIhl**2 + (ghl*sdIother)**2]
               against sdrej2, where Iother = the other observation
        (b)
               if either Delta(hl) > sdrej2, then
         1. in scaling, reject reflection. Or:
         2. in merging,
         1. keep both (default or if KEEP subkey given) or
         2. reject both (subkey REJECT) or
         3. reject larger (subkey LARGER) or
         4. reject smaller (subkey SMALLER).

   (2)
   if there 3 or more observations left, then
   (a)
          for each observation Ihl,

    1. calculate weighted mean of all other observations <I>n-1 & its
       sd(<I>n-1)
    2. deviation
          Delta(hl) =
       |Ihl - ghl <I>n-1>| / sqrt[sigIhl**2 + (ghl*sd(<I>n-1))**2]
    3. find largest deviation max|Delta(hl)|
    4. count number of observations for which |Delta(hl)| .ge. 0 (ngt), &
       for which |Delta(hl)| .lt. 0 (nlt)

   (b)
   if max|Delta(hl)| > sdrej, then reject one observation, but which one?
    1. if ngt == 1 .or. nlt == 1, then one observation is a long way from
       the others, and this one is rejected
    2. else reject the one with the worst deviation max|Delta(hl)|

   (3)
   iterate from beginning
     _________________________________________________________________

RELEASE NOTES

Version 3.1.20

     * Fixed bug for files lacking XDET, YDET

Version 3.1.19

     * Fixed bug for BATCH BFACTOR mode in working out "best" batch

Version 3.1.18

     * Corrected totals in harvest file

Version 3.1.15

     * Fixed long-standing bug in resolution limits for analysis, when
       resolution is cut back from maximum in the MTZ file

Version 3.1.12

     * Fixed bug in BATCH mode when runs are automatically allocated

Version 3.1.6-11

     * Default maximum width of partials to 5 degrees
     * Minor syntax changes to keep compilers happy
     * Extend partial bias analysis to case when there are no fulls,
       correct small bug in previous analysis
     * Correct (again) case of no datasets defined in file

Version 3.1.5

     * In Project & dataset names, only accept alphanumeric and "-._"
       characters, change others to "_"
     * fixed bug in dtsstore routine (failed with 5 or more datasets)
     * defaults BASE dataset = 1 if no wavelength information in file

Version 3.0.N, 3.1.2-4

     * Many changes to handle multiple datasets properly
     * REJECT BYRUN option removed, replaced by COMBINE to do the
       opposite
     * Analysis of correlation and differences between datasets, for MAD
     * TIE BFACTOR
     * NORMALISE to allow normalisation of Bfactor on best bit
     * Wrap-around of Phi at 360 degrees
     * Fixed bug in anomalous normal probability plot
     * Added SCALES SMOOTH option
     * Automatic assignment of runs
     * TIE A1 option, and auto-fixing of tails parameters
     * OUTPUT BEAMS option
     * EXCLUDE BATCH, DATASET, CRYSTAL options
     * SCALES ABSORPTION option
     * default Bfactor smoothing made less smooth (Vwt = 0.5 instead of
       1.0). This seems to improve behaviour (reduces oscillations)
     * Absorption options now use datum setting in orientation block if
       set (relevent for 3-circle goniostats for ABSORPTION option)

Version 2.7.6

     * Corrected B-factor in analysis table against batch when it is a
       function of TIME.

Version 2.7.5

     * Added EXCLUDE ARC option

Version 2.7.4

     * Added OUTPUT POLISH option

Version 2.7.3

     * Bug fix: "output separate" now works again

Version 2.7.2

     * Correct calculation of completeness, by counting reflections,
       instead of approximate calculation by volume.

Version 2.7.1

     * Harvest stuff added by Martyn Winn & Kim Henrick
     * Corrected bug in counting rejections by batch

Version 2.6.4

     * Set SDADD parameter = 0.02 by default
     * New algorithm to determine initial scales from mean intensities:
       this should work much better when different runs or batches have
       very different resolution ranges.

Version 2.6.3

     * Default to include summed partials in scaling
     * Classify partials for analysis in the batch to which they
       contribute most, rather than to the first batch they occur in.

Version 2.6.2

     * Allow extrapolation of RESTORE file to new batches
     * Buffer input echo so that there is a plain text & html form

Version 2.6.1

     * Fixed pointer bug in FIX

Version 2.6.0

     * Spherical harmonic expansion of scale factors: SCALES SECONDARY &
       SCALES SURFACE options

Version 2.5.5

     * Added EXCLUDE EMAX|EPROB option, to reject zingers & ice spots
       (Read's method)
     * Added unit weight option CYCLES WEIGHT UNIT
     * Added calls to libhtml to write html stuff into log file

Version 2.5.4

     * New optional outlier check comparing I+ with I- observations in
       ANOMALOUS ALL case (REJECT ... ALL)
     * Removed all (or most) html-reserved characters from logfile

Version 2.5.3

     * Checks on PhiRange if present

Version 2.5.2

     * Proper default for PARTIAL TEST (s/r chkkpf)
     * Count failures with inconsistent MPART flags

Version 2.5.1

     * Fixed uninitialized variables in s/r setscl, particularly
       affecting eg "scales batch detector 3 3"
     * Updated version of ea06cd

Version 2.5.0

     * Includes all Kim Henrick's harvesting calls, and calls to new MTZ
       library things for project & dataset names, but currently
       commented out or inactivated

Version 2.4.3

     * Fixed a couple of uninitialized variable bugs (in s/r anlini,
       nrmprb)

Version 2.4.2

     * New REJECT options for two observations (KEEP, REJECT, LARGER,
       SMALLER)

Version 2.4.1

     * Allow for MPART > 200, for Mosflm 5.51
     * Corrected partial check, to allow for errors in MPART

Version 2.3.2

     Out of Phi range is warning, not fatal

     Check for M>0 (flag set in Postref) for partials: previously didn't
   work with data from Postref

     Correct labels for UNMERGED output option

     DAMP keyword added

     Bug fix to avoid normal probability analysis problem is no fulls

Version 2.3.1

     Output labels for SEPARATE option changed to conform with CCP4 3.3
   convention, i.e. I(+) and I(-) etc

Version 2.3.0

     added "anomalous match" options for selecting matched I+ & I-

     EXCLUDE does not check reference batch

  Version 2.2.3

    1. fixed bug in summed partials in case of "scales batch": this
       combination is still dubious, but awaits proper analysis
    2. added PARTIALS keyword
    3. fixed bug in calculation of Rfull: this was completely wrong if
       anomalous data was present
    4. added INTENSITIES ANOMALOUS option to keep I+ & I- separate in
       scaling (not normally recommended)
    5. allow incomplete orientation data in certain cases

  Version 2.2.2, November 1996

    1. defaults on partial summation improved (and again 18/12/96)
    2. analysis on fulls only even when partials are used
    3. bug fix in random number routine (thanks to Adam)
    4. ONLYMERGE option
    5. If scaling across detector (e.g. "scales detector 3 3"), checks on
       valid Xdet, Ydet (within limits in file header)
    6. Rogues file lists Xdet, Ydet, Phi
    7. default in scaling is "exclude sdmin 6" (omitting weak
       observations speeds scaling)
    8. default FIX A0
    9. reject outliers on every cycle if scales "restored" (else previous
       scaling gets messed up)
   10. analysis by position on detector
   11. fixed bug affecting "reject byrun" & deviations with anomalous on

  Version 2.2.1, November 1996

   Many changes from version 1.x.x
    1. this version by default merges multiple measurements and thus
       replaces Agrovata. See the keyword OUTPUT for further description
       of the output options:-

        -
                AVERAGE [default] merged I (as from Agrovata)
                SEPARATE separate scaled measurements (as from older
                Scala versions), for reinput into Scala, or input into
                Agrovata [not recommended]
                POSTREF scaled file for input to POSTREF
                UNMERGED scaled, partials summed (or scaled), but not
                merged

    2. by default, the SDCORRECTION parameter SdFac (multiplier) will be
       automatically adjusted, from the normal probability analysis of
       deviations. This is done in a separate pass through the data
       before the final merging pass. The command SDCORRECTION NOADJUST
       disables this adjustment.
    3. The scaling option TAILS has been introduced. This makes some
       attempt to correct for the different truncation of the tails of
       diffuse scattering between fulls & partials. This option comes
       with a health warning: it should be treated with caution. Try with
       & without. (see commands SCALES . . TAILS, FIX, [UN]LINK)
    4. the way of putting data (e.g. native) back into the scaling as a
       reference set has changed. See example.
    5. treatment of summed partials has been elaborated (see FINAL &
       INTENSITIES keywords above). In 2.2.1, the defaults are not set
       optimally (whatever that means!): this is improved in 2.2.2
       Recommended usage:
FINAL PARTIALS CHECK TEST 0.95 1.05     # for Mosflm

FINAL PARTIALS TEST 0.95 1.05         # for Denzo (but FractionCalc
                                      #  is rather unreliable)

    6. Scales are dumped to the file SCALES by default (see DUMP &
       RESTORE)
    7. Normal probability analyses done, plots output to files NORMPLOT
       and ANOMPLOT in a format sutiable for xmgr (from your favourite
       ftp server)
    8. by default scaling now excludes weak data (EXCLUDE SDMIN 3.0)

AUTHOR

   Phil Evans, MRC Laboratory of Molecular Biology, Cambridge
   (pre@mrc-lmb.cam.ac.uk) See above for Release Notes.

SEE ALSO

   truncate, postref, Data Harvesting