SIGMAA (CCP4: Supported Program)
                                       
NAME

   sigmaa - Improved Fourier coefficients using calculated phases
   
SYNOPSIS

   sigmaa HKLIN foo_in.mtz [ HKLOUT foo_out.mtz ]
   [Keyworded input]
   
DESCRIPTION

   The program SIGMAA (Read, 1986) can be used to combine a set of
   calculated phases with a set of previously determined phases for which
   the phase probability profiles are held in the form of
   Hendrickson-Lattman coefficients.
   
   It calculates weighted Fourier coefficients either from the calculated
   phase from a (partial) model structure, or by combining phase
   probabilities from isomorphous phases with those from one or more
   (partial) structures.
   
   WARNING: SIGMAA has been converted so that it will work with MNFs. In
   a similar fashion to FFT (see also documentation on Missing Number
   Flags); Fo will be replaced by DFc, if it is missing, for the FWT map
   coefficient. Also, when combining phases of missing data, the phase
   probability will be assumed to be uniform. However, the procedure may
   not be optimal, hopefully a version from Randy Read will be available
   in a subsequent version.
   
   There are 3 main options:
    a.
       
        PARTIAL
                use partial structure information, writing out a weight
                and coefficients for maps in columns as follows:
                
              WCMB
                      A weight (analagous to `Sim weight') to estimate
                      the reliability of AlphaCalc.
                      
              DELFWT (m|Fo| - D|Fc|) exp(i AlphaCalc)
                      For a difference map, FFT input: F1=DELFWT PHI=PHIC
                      
              FWT (2m|Fo| - D|Fc|) exp(i AlphaCalc)
                      Analogous to 2Fo-Fc map, FFT input: F1=FWT PHI=PHIC
                      
                where Fo, Fc are observed and calculated structure
                factors. Note that for centric terms, the (2m|Fo|-D|Fc|)
                coefficients are replaced by m|Fo|; these coefficients
                reduce/remove model bias.
                
    b.
       
        COMBINE PART
                combine isomorphous phase (preferably input by
                Hendrickson-Lattman coefficients ABCD) with calculated
                phases from up to 3 sources; output the combined phase
                (PHCMB WCMB) and coefficients which minimise model bias.
                (labelled again: FWT PHFWT and DELFWT PHDELFWT)
                
    c.
       
        COMBINE MIR2
                combine two sets of experimental phases with or without
                Hendrickson-Lattman coefficients. This can only be done
                pair-wise, it might be argued that instead all data
                should be used in calculating the phase.
                
   The program first calculates, iteratively in resolution bins, the
   value of SigmaA as defined by Srinivasan, 1966; and then for each
   reflection, the figure of merit m and the estimate of the error in the
   partial structure from coordinate errors D (Luzzati, 1952). There is
   an option to scale these to modify the weight assigned to the partial
   structure information, or to read in values of SigmaA derived
   previously.
   
   If EPS is the multiplicity for the reflection zone (Rogers, 1965),
           SigmaA = D*sqrt(sigmaP/sigmaN)
             Eo   = Fo/sqrt(EPS*sigmaN)
       and   Ec   = Fc/sqrt(EPS*sigmaN)
    where  sigmaN = <Fo**2/EPS> and sigmaP = <Fc**2/EPS>.

   The figure of merit m = <cos(AlphaTrue - AlphaCalc)> is calculated
   from Eo, Ec and SigmaA, while the map coefficients arise from the
   approximation that
    m Eo exp(iAlphaCalc) = 0.5 Eo exp(iAlphaTrue)
                          +  0.5 SigmaA Ec exp(iAlphaCalc)

   If coordinate errors are assumed to be normally distributed,
    ln SigmaA = intercept - slope * (sintheta/lambda)**2
       where intercept = 0.5 * ln(sigmaP/sigmaN)
         and     slope = pi**3 * (mean square coordinate error)

KEYWORDED INPUT

   The various data control lines are identified by keywords. Only the
   first 4 characters need be given. Those available are:
   
     COMBINE, END, ERROR, LABIN, LABOUT, PARTIAL, RANGES, RESOLUTION,
     SIGMAA, SYMMETRY, TITLE
     
  COMBINE [ PART <nps> ] [ DAMP <d1> [ <d2> [ <d3> ]]] [ RESOLUTION <Rmin>
  <Rmax> ]
  
   [Required for option (b).]
   
   Use this option to combine experimental phase information from
   isomorphous replacement (columns PHIBP, WP, HLA, HLB, HLC, HLD from
   the input data file) with that from (partial) model structures. This
   option produces an output data file assigned to HKLOUT.
   
   PART <nps>
          <nps> is the number of (partial) model structures, default: 1,
          maximum allowed: 3.
          
   DAMP <d1> <d2> <d3>
          <d1> <d2> <d3> (default 1.0) are values to multipy the SigmaA
          values generated for the partial structures. Once the Rfactor
          between Fobs and Fcalc is below 30% or thereabouts the SigmaA
          Weights become close to 1. This means that there will be very
          little contribution to the combined phase from the MIR
          information. Giving values of di<1.0 may be helpful. See
          keyword SIGMAA for Randy's preferred solution.
          
   RESOLUTION <Rmin> <Rmax>
          If resolution limits <Rmin>, <Rmax> are given here, phase
          combination is only done within this resolution shell:
          typically this would be used to include experimental phases
          only for high resolution data during a phase extension process.
          In this case, a low resolution limit would be set, allowing
          lower resolution data which has already been phased in previous
          cycles to diverge from the (incorrect) experimental phases
          according to phase information from averaging or density
          modification.
          
  COMBINE [MIR2] [ RESOLUTION <Rmin> <Rmax> ]
  
   Merge together two sets of MIR phases. RESOLUTION is the same as
   above.
   
  ERROR
  
   If this command is present, a straight line is fitted to the plot of
   ln (SigmaA) against resolution in order to estimate the rms coordinate
   error.
   
  LABIN <program label>=<file label> .....
  
   Input column assignments. Program labels for the various options are:
   
   PARTIAL
          FP SIGFP FC PHIC
          
   COMBINE PART ...
          FP SIGFP PHIBP WP [HLA HLB HLC HLD], with FC PHIC or FC1 PHIC1
          FC2 PHIC2 [FC3 PHIC3]
          
   COMBINE MIR2 ...
          FP SIGFP PHIBP WP [HLA HLB HLC HLD], with PHIB2 W2 [HLA2 HLB2
          HLC2 HLD2]
          
  LABOUT <program label>=<file label> .....
  
   Output column assignments. Program labels for the options producing
   output data are:
   
   PARTIAL
          DELFWT FWT WCMB
          
   COMBINE MIR2
          HLAC HLBC HLCC HLDC WCMB PHCMB
          
   COMBINE PART ...
          DELFWT PHDELFWT FWT PHFWT WCMB PHCMB For details of these, see
          INPUT AND OUTPUT FILES.
          
  PARTIAL [ DAMP <d1> ]
  
   Produce weighted map coefficients from a partial structure. This is
   the default option. It produces an output .mtz data file.
   
   DAMP <d1>
          <d1> is the damping factor for the SigmaA weights (default
          1.0).
          
  RANGES [ <nbin> <mon> ]
  
   Set the number of resolution bins <nbin> and the reflection monitoring
   interval <mon>. Defaults: 20 1000; maximum <nbin> allowed: 50.
   
   <nbin> is the number of resolution bins (equal width in
   [sin(theta)/(lambda)]**2 in which to divide partial structure data for
   normalization and sigmaA estimation. It is IMPORTANT that resolution
   ranges contain sufficient reflections. It is best to use as large a
   value of <nbin> as possible, as long as the estimates of sigmaA vary
   smoothly with resolution. If they do not, <nbin> should be reduced
   until sigmaA does vary smoothly. A good first guess is the number of
   reflections divided by 1000. If sigmaA refinement converges to zero in
   one or more of the ranges (which happens sometimes when the correct
   value is low), this can usually be circumvented by decreasing <nbin>.
   
   Information about every <nmon>-th reflection will be written to the
   log file.
   
  RESOLUTION [ <rmin> ] <rmax>
  
   Low and high resolution limits in either order or upper limit if only
   one is specified. These may are in Angstroms or if both are <1.0,
   units of 4(sintheta/lambda)**2. By default, all the data in the file
   are used.
   
  SIGMAA <nps> <nbin>
  
   Input SigmaA values from another source. Normally these values will be
   calculated in the program so this keyword is unnecessary. However if
   the agreement between Fobs and Fcalc becomes very good - for example
   if the Rfactor is <25% - then the calculated SIGMAA values weight up
   the PHIcalc at the expense of the experimental phases. This may not be
   desirable and you may need either to invoke the DAMP keyword or retain
   an early estimate of sigmaA.
   
   <nps>
          number of partial structures.
          
   <nbin>
          number of bins, followed by <nbin> lines of the form:
          
 SigmaA(1,1)    [ SigmaA(2,1)  ...   [SigmaA(nps,1)]]
 SigmaA(1,2)    [ SigmaA(2,2)  ...   [SigmaA(nps,2)]]
  ..........
 SigmaA(1,nbin) [ SigmaA(2,nbin) ... [SigmaA(nps,nbin)]]

  SYMMETRY <name> | <number> | <operators>
  
   Spacegroup number or name or operators in International Tables format.
   By default, symmetry information is read from the input file header.
   
  TITLE <title>
  
   A title written to the log file and in the header of the output MTZ
   data file (if produced).
   
  END
  
   End of input.
   
INPUT AND OUTPUT FILES

  Input reflection data file
  
   This is an MTZ file assigned to logical name HKLIN. The following
   column assignments are required (those which are optional are enclosed
   in square brackets):
    a.
       
        PARTIAL option:
                H K L FP SIGFP FC PHIC
                with
                
              FP, SIGFP
                      native amplitude and standard deviation
                      
              FC, PHIC
                      calculated amplitude and phase (degrees)
                      
    b.
       
        COMBINE option:
                
         i.
            
              Combination of two sets of MIR phases:
                      H K L FP SIGFP PHIBP WP [HLA HLB HLC HLD]
                      PHIB2 W2 [HLA2 HLB2 HLC2 HLD2]
                      with
                      
                    FP, SIGFP
                            native amplitude and standard deviation
                            
                    PHIBP
                            isomorphous centroid phase (degrees)
                            
                    WP
                            figure of merit
                            
                    HLA...HLD
                            Hendrickson-Lattman probability coefficients
                            corresponding to isomorphous phase. If these
                            are absent, a unimodal probability
                            distribution will be set up around PHIBP.
                            
                    PHIB2
                            isomorphous centroid phase for second set
                            
                    W2
                            figure of merit for second set
                            
                    HLA2..HLD2
                            Hendrickson-Lattman probability coefficients
                            for second set. If these are absent, a
                            unimodal probability distribution will be set
                            up around PHIB2.
                            
        ii.
            
              Combination of one set of MIR phases with PARTIAL
                      information:
                      H K L FP SIGFP PHIBP WP [HLA HLB HLC HLD]
                      plus FC PHIC
                      or FC1 PHIC1 FC2 PHIC2 [FC3 PHIC3]
                      with
                      
                    FP, SIGFP
                            native amplitude and standard deviation
                            
                    PHIBP
                            isomorphous centroid phase (degrees)
                            
                    WP
                            figure of merit
                            
                    HLA...HLD
                            Hendrickson-Lattman probability coefficients
                            corresponding to isomorphous phase. If these
                            are absent, a unimodal probability
                            distribution will be set up around PHIBP.
                            
                    FC, PHIC
                            calculated amplitude and phase (degrees) for
                            one partial structure
                            
                    FC1, PHIC1
                            calculated amplitude and phase (degrees) for
                            first partial structure when nps > 1
                            
                    FC2, PHIC2
                            calculated amplitude and phase (degrees) for
                            second partial structure when nps = 2
                            
                    FC3, PHIC3
                            calculated amplitude and phase (degrees) for
                            third partial structure when nps = 3
                            
  Output reflection data file
  
   This is an MTZ file assigned to logical name HKLOUT. The file will
   contain all the columns from the input file with extra columns
   appended, the number depending on which option was used. The default
   labels of these columns are given below; these may be changed with
   LABOUT command.
    a.
       
        PARTIAL option:
                The new columns are: WCMB DELFWT FWT, with
                
              WCMB
                      figure of merit m of calculated phase (Sim weight)
                      
              DELFWT
                      Fourier amplitude for `difference' map (mFo-DFc)
                      
              FWT
                      Fourier amplitude for '2Fo-Fc' map (2mFo-DFc) These
                      terms may be positive or negative.
                      
       The phases used for these maps will always be PHIC.
    b.
       
        COMBINE option:
                The new columns are: PHCMB WCMB FWT PHFWT DELFWT
                PHDELFWT, with
                
              PHCMB
                      combined phase angle (degrees)
                      
              WCMB
                      combined figure of merit
                      
              FWT
                      Fourier amplitude for '2mFo-DFc' map
                      
              PHFWT
                      Combined phase for this term
                      
              DELFWT
                      Fourier amplitude for 'mFo-DFc' map
                      
              PHDELWT
                      Combined phase for this term
                      
AUTHORS

   Originator: August 1986: R.J. Read.
   
   Incorporates updates from [11].
   
EXAMPLES

  Difference and 2Fo-Fc maps from calculated phases
  
sigmaa HKLIN hktmpico.mtz HKLOUT hksigmaa1.mtz
TITLE   SIGMAA m*Fo-Fc map  pfk B.st. BP2.. PROLSQ cycle<1>..
RESOLUTION 100.0 2.6 ! Resolution limits in Angstroms
RANGES   30 5000     ! Number of bins for analysis v. resolution
                     ! Monitor every 5000th reflection
PARTIAL              ! Option for difference map coefficients
ERROR                ! Use sigmaA v resolution for coordinate error
LABIN FP=FO SIGFP=SIGFO FC=FC PHIC=PHIC
END

   Note: This example uses the default output file labels. To calculate
   the `difference' map, use DELFWT in FFT. To calculate the `2Fo-Fc'
   map, use FWT.
   
  Phase combination
  
sigmaa
HKLIN ../data/sp400_monster2.mtz
HKLOUT ../data/sp400_phase_comb.mtz
<< END-sigmaa
TITLE   TRYIT
RANGES  10 1000      ! Number of analysis bins, monitor interval
RESOLUTION 0.0 0.25  ! Resolution limits in 4(sintheta/lambda)**2
ERROR                ! Use sigmaA v resolution for coordinate error
COMBINE PART 1       ! Combine isomorphous + 1 partial model
LABOUT  PHCMB=PHCMB WCMB=WCMB FWT=FWT PHWT=PHWT
LABIN   FP=F(Mer) SIGFP=SIGF(Mer) PHIBP=PHIBEST WP=FOM -
        HLA=A HLB=B HLC=C HLD=D -
        FC=FC PHIC=AC
END
END-sigmaa

NOTES

  Phase combination
  
   The phase combination method used in sigmaa depends on the Hendrickson
   and Lattman (1970) formulation of the phase probability profile for a
   phase Alpha:
  P(Alpha) = exp(A cosAlpha + B sinAlpha + C cos2Alpha + D sin2Alpha)

   A, B, C, D are known as the phase coefficients. Phase information from
   different sources can be combined by a simple addition of the phase
   coefficients from each determination. The application of a weighting
   scheme proposed by Sim (1959) allows for the inclusion of phase
   information determined from a partial structure.
   
   The principles of the method and details of the original phase
   combination program are described by Bricogne (1976).
   
  Model bias on combination
  
   It is assumed that the coefficients giving least bias vary as a linear
   function of partial structure influence. The variation of information
   is the parameter used to measure the contribution of each partial
   structure to the combined phase probability profile; and this is
   normalised to give partial structure weights w. These are tabulated as
   a function of resolution in the log file. If there are p partial
   structures, the modified map coefficients are given by
         [2mFo - sum_over_p(wDFc)] / [2 - sum_over_p(w)]

REFERENCES

    1. Read, R.J.: Acta Cryst. A42 (1986) 140-149.
    2. Srinivasan, R.: Acta Cryst. 20 (1966) 143-144.
    3. Hauptman, H.: Acta Cryst. A38 (1982) 289-294.
    4. Luzzati, V.: Acta Cryst. 6 (1953) 142-152.
    5. Rogers, D. in Computing Methods in Crystallography (Rollett,
       J.S.,ed.) (1985) pp. 126-127, Pergamon Press.
    6. Hendrickson, W.A. & Lattman, E.E.: Acta Cryst. B26 (1970) 136-143.
    7. Bricogne, G.: Acta Cryst. A32 (1976) 832-847.
    8. Sim, G.A.: Acta Cryst. 12 (1959) 813-815; 13 (1960) 511-512.
    9. Read, R. J.: Acta Cryst. A46 (1990) 140-9.
   10. Read, R. J.: Acta Cryst. A46 (1990) 900-12.
   11. Vellieux, F.M.D., Livnah, O., Dym, O., Read, R.J. & Sussman, J.L.,
       manuscript in preparation.