TLSANL (CCP4: Supported Program)
                                       
NAME

   tlsanl - analysis of TLS tensors and derived anisotropic U factors
   
SYNOPSIS

   tlsanl xyzin input.brk tlsin input.tls xyzout output.brk [ axes
   output.in ]
   [Keyworded input]
   
DESCRIPTION The program analyses TLS tensors and is intended for use with the
output of RESTRAIN or REFMAC.

INPUT AND OUTPUT FILES

  TLSIN
  
An ASCII file containing details of the TLS groups and the values of the
corresponding T, L and S tensors. See the RESTRAIN documentation for details of
the file format. In addition to the records described there, the file may
contain a line "REFMAC" denoting that the file has been output from the
refinement program REFMAC, which has a different order of tensor elements.

  XYZIN
  
   Input coordinates in PDB format. ANISOU records are ignored. ATOM
   records may contain the full B factor (as output by RESTRAIN) or only
   the residual B factor (which doesn't include the contribution from the
   TLS parameters, as output by REFMAC). The program interprets the B
   factors according to the keyword BRESID.
   
  XYZOUT
  
   Output coordinates and anisotropic tensors in PDB format. The ATOM
   records may contain the full B factor, the residual B factor, or the
   TLS-component of the B factor according to the keyword ISOOUT. The
   ANISOU records contain the full anisotropic displacement parameters,
   irrespective of the ISOOUT keyword.
   
  AXES
  
   Output file containing the axes for translation, libration,
   screw-rotation, reduced translation and non-intersecting
   screw-rotation. The file is in a suitable format for including in a
   MOLSCRIPT .in file. See AXES keyword below.
   
KEYWORDED INPUT

Available keywords are:

     ANISO, BINPUT, BRESID, ISOOUT. AXES. END,
     
  ANISO
  
   Do anisotropic tensor analysis (default: don't). The principal axes of
   the anisotropic tensor are determined for each atom in each TLS group
   and written to the log output. If the tensor is non-positive definite,
   then a warning is given. The anisotropic tensor includes the isotropic
   contribution as well as the contribution from the TLS parameters.
   
  BINPUT [true | t | false | f]
  
   If true (default), assume PDB file contains isotropic B factors. Else,
   assume PDB file contains isotropic U factors (smaller by 8*pi**2).
   
  BRESID [true | t | false | f]
  
   If true, assume the ATOM records in XYZIN contain only residual B
   factors, and don't include the contribution from the TLS parameters.
   If false (default), assume the ATOM records contain the full B factor,
   including the contribution from TLS.
   
  ISOOUT [FULL | RESI | TLSC]
  
   Determine whether the ATOM records in XYZOUT contain B factors
   calculated from the TLS parameters (TLSC), residual B factors (RESI),
   or the sum of both (FULL). Default is FULL.
   
  AXES [ < scale > ]
  
   A file (logical name AXES) is output containing the axes for
   translation, libration, screw-rotation, reduced translation and
   non-intersecting screw-rotation, for each TLS group. All axes are
   calculated in an orthogonal frame with respect to the centre of
   reaction. The file is in a suitable format for including in a
   MOLSCRIPT .in file.
   
   Each axis is written as a pair of coordinates (in the coordinate
   system of the input PDB file) representing the beginning and the end
   of the axis. For the intersecting axes, the intersection is at the
   centre of reaction of the TLS group. The length of each axis is
   proportional to the magnitude of the corresponding motion. The
   proportionality factor can be adjusted by the argument < scale >,
   which defaults to 10.
   
  END
  
   Terminate input.
   
PROGRAM OUTPUT

   For each TLS group included in the file TLSIN, the program outputs
   information about the TLS tensors in several representations. Two
   coordinate origins are considered:
    1. The origin used in refinement, and given by the ORIGIN record in
       TLSIN.
    2. The centre of reaction, which is the origin that makes S
       symmetric. TLS tensors with respect to this origin are flagged
       with a prime (').
       
   Three axial systems are considered:
    1. Orthogonal axes, as used in XYZIN and TLSIN
    2. Libration axes, i.e. the principal axes of the L tensor. TLS
       tensors in this axial system are flagged with a caret (^).
    3. Rigid-body axes.
       
   The values of the T, L and S tensors are given with respect to both
   origins, and in the first two axial systems. The L tensor is in
   general independent of the origin, and in particular is the same for
   both origins considered here. In the axial system defined by the
   libration axes only, the diagonal elements of S are also independent
   of origin.
   
   The values of the T and S tensors held in TLSIN thus depend on the
   origin chosen for their calculation. The Centre of Reaction, however,
   is independent of the original origin, and hence so are quantities
   calculated with respect to the Centre of Reaction.
   
   The rigid body motion can also be described as 3 screw motions about 3
   non-intersecting axes parallel to the libration axes, together with a
   reduced translation tensor (see Schomaker and Trueblood (1968)). The
   program gives the absolute position of these screw axes and the pitch
   of the screw motion along them, followed by the reduced translation
   tensor.
   
EXAMPLES For files generated by RESTRAIN, defaults can be accepted, although
the ANISO keyword might be useful:


tlsanl XYZIN foo_in.pdb TLSIN foo_in.tls XYZOUT foo_out.pdb <<eof
ANISO
END
eof

   For files generated by REFMAC, the BRESID keyword will be needed:

tlsanl XYZIN foo_in.pdb TLSIN foo_in.tls XYZOUT foo_out.pdb <<eof
BRESID
END
eof

REFERENCES

    1. B.Howlin, S.A.Butler, D.S.Moss, G.W.Harris and H.P.C.Driessen,
       "TLSANL: TLS parameter analysis program for segmented anisotropic
       refinement of macromolecular structures.", J. Appl. Cryst., 26,
       622-624 (1993)
    2. V.Schomaker and K.N.Trueblood Acta Cryst., B24, 63 (1968)
       
SEE ALSO

   restrain, refmac
   
AUTHORS

   Huub Driessen, David Moss, Ian Tickle et al., Birkbeck College.
   
   Contact: Ian Tickle (tickle@mail.cryst.bbk.ac.uk), Martyn Winn
   (m.d.winn@dl.ac.uk)